## Slide 1: Analog Circuit and Layout Synthesis Revisited
Rob A. Rutenbar Bliss Professor and Head

## Slide 2: A Talk in 3 Parts
Looking back: Analog history in review
Reflection: What we got right (& not…)
Looking forward: New opportunities

## Slide 3: Looking Back….
-
+

## Slide 4: A Little Analog History…
In first decade (more or less) of 21st century, lots of startups doing first ‘real’ products, based on previous decade of R&D

## Slide 5: A Little History…
Most of them died; a few got bought by big EDA players; technologies added to big, flagship analog/mixsig platforms

## Slide 6: We Made Some Real Progress
Digital Methodology
  Synthesis
  Optimization
  Verification
  Reuse & IP
Analog Methodology
  Toward Synthesis
  Toward Layout
  Toward Stat Optimize
  Toward Reuse & IP

## Slide 7: Core Strategy: Optimization-Based Design
All successful approaches have this overall structure
Use some clever form of heuristic or numerical search
  Optimization engine: proposes candidate circuit solutions
  Evaluation engine: evaluates quality of each candidate
  Cost-based search: cost metric represents “goodness” of design
Evaluated
Circuit
Performance
Candidate
Circuit
Design
Optimization
Engine
Evaluation
Engine

## Slide 8: Key Example: Sizing/Centering Tools
For device-level ckt design, you have to do these tasks
Gain 60dB
UGF 111MHz
Phase 60deg
Slew 2V/us
CMRR: 60dB
PSRR: 70dB
THD: 1%
...
Generate
proper
specs
Design
proper
circuit topology
Design
proper device
sizing/biasing
80/4
80/4
Optimize for
centering,
yield
Optimization works well here

## Slide 9: Some Commercial Successes
BIASING
AMPLIFIER
Ex: Sizing (and also layout) very useful for migration
Can size, optimize for perform/yield, layout, migrate …
STMicroelectronics result [Shah, Dugalleix, Lemery DATE02]
Area: ~9000 mm2
Power: 9.15mW
Auto
Sizing
Auto
Layout
180nm
Both sizing and layout
0.12
m
m
Area: ~4000 mm2
Power: 1.1mW
Auto
Sizing
Auto
Layout
120nm
[Source: Cadence]

## Slide 10: This is the Landscape that Emerged…
hour
day
week
month
year
hour
day
week
month
year
How long to setup?
How long
to run?
Simulation-based tools (“SPICE-in-the-loop”)
  PRO: same setup as validation
  PRO: quicker to set up
  CON: slowest to run; scaleup?
Analytical modeler tools (“convex”, “smooth” etc)
  PRO: run really, really fast
  PRO: scale up to big things
  CON: long setup; accuracy?
Ex: Cadence Virtuoso ADE
Ex: Magma (SNPS) Titan AVP

## Slide 11: Core Layout Model: Design at 3 Levels
CELL
SYSTEM
DEVICE
Devices play role like gate-level cells in digital ASIC, but more complex, malleable; we need device-generators
Macroscopic level, its all more like floorplanning, placement, routing

## Slide 12: Analog Layout: DeviceGen + Place/Route
To first order, this is a (very constrained) place/route task…
But with very complex generators for atomic pieces (devices)
Source: Cadence
Image provided by ©2010 Cadence Design Systems, Inc.
All rights reserved worldwide

## Slide 13: {Topologies+Sizing+Layout}  Soft IP Library
A library of topologies, constraints, and validation (sim) steps

## Slide 14: Again, Some Commercial Successes…
Courtesy: Neolinear, Cadence
Handcrafted
Automatic Place/Route

## Slide 15
So, despite successes, why is analog NOT just ‘solved’ …?

## Slide 16: Pause, Reflect…
-
+
?
…first, I propose to commit Philosophy
(I warned you….)

## Slide 17: Aggressive Philosophical Proposition…
There are, in real world, only 2 kinds of EDA tools
INSURANCE
PAIN RELIEF
…and you must figure out what kind you are building

## Slide 18: Lessons Learned from First-Gen Tools
Things we got RIGHT
  Tools based on optimization
  Models & setup for custom design are critical synthesis IP
  Tools embedded in same design flows as manual ckt design
  Divide & conquer (capture/synth/gen/P&R, etc) critical
Things we MISSED
  Usage models – how real people do real designs
  (I’ve called this “the Sociology of Circuit Design”)

## Slide 19: My 1st Generation of Sizing Synthesis Tools
Built Sizing Optim
Then Constraint Mgr
Then Statistical Centering
Expected
Designer
Interest
Sizing
Constraint
Manage
Statistical
Center

## Slide 20: My 1st Generation of Sizing Synthesis Tools
Built Sizing Optim
Then Constraint Mgr
Then Statistical Centering
Actual
Designer
Interest
Constraints
Statistical
Center
Sizing

## Slide 21: Why this “Inversion” of Tool Interest
Revisit the sociology of the problem
Question: Is circuit sizing/biasing difficult (painful?) YES
Question: Will circuit design experts admit this? NO
Question: Is circuit centering for statistics painful? YES
Question: Will circuit design experts admit this? YES
Question: Is circuit setup for IP reuse painful? YES
Question: Will circuit design experts admit this? YES

## Slide 22: 1st Gen Synthesis Tools Revisited
Built Sizing Optim
Then Constraint Mgr
Then Statistical Centering
Actual
Designer
Interest
Constraints
Statistical
Center
Sizing

## Slide 23: My 1st Gen of Layout Synthesis Tools
Placer
Router
Gen
Built Device Generators
And Placer
And Router
Expected
Designer
Interest

## Slide 24: My 1st Gen of Layout Synthesis Tools
Built Device Generators
And Placer
And Router
Actual
Designer
Interest
Placer
Router
Gen

## Slide 25: Why? #1 Your Schematic is NOT What You Lay Out
Analogy: Tech Mapping in ASIC
Map to what can really work in layout
Groups of devices w/ complex constraints
Surprise: enormous pain here to get right; gen’s reduce layout time & reduce size (a lot)
COMPLEX PLACEMENTS INSIDE GENERATORS
COMPLEX ROUTING INSIDE GENERATORS

## Slide 26: Surprising, Rich PD Area: Optimizers+Shapes+People

## Slide 27: Why #2: Curse of Analog Aesthetics…
A thought experiment: I want 12 analog layouts of same ckt

## Slide 28: Why #2: Curse of Analog Aesthetics…
Experimental method: 11 layout experts && 1 CAD tool

## Slide 29: Why #2: Curse of Analog Aesthetics…
Probability1, will get 12 different layouts, all correct

## Slide 30: Why #2: Curse of Analog Aesthetics…
Probability1, all humans think all other layouts look “wrong”
???

## Slide 31: The Problematic Sociology of Analog Aesthetics
Why this remarkable, relentless focus on “my way” of layout?
Aesthetics is often a surrogate for correctness
  Not everything that matters in analog is robustly – or even explicitly, and correctly – represented in the design process.
  Consequence: Aesthetics used for insurance!
Hey, that looks strange, right?

## Slide 32: Aesthetic Engineering Dominates Analog Layout
This does not happen when you design 100M digital gates…
Copyright © 1993, The National Gallery, London
Copyright © 1993, The National Gallery, London
Why? Pain relief
of automation
is JUST SO BIG

## Slide 33: Nevertheless—Many Successes, and Surprises
If it wasn’t really good, perhaps nobody would be stealing it…
Google’s helpful link to recipe to steal our circuit synthesis tool
For my CDNS friends: yes, link is now DEAD

## Slide 34: Nevertheless—Many Successes, and Surprises
How much do designers like smart device generators (the Cadence ModGen tools)…?

## Slide 35: Future Opportunity….
-
+

## Slide 36: Ongoing Analog Bifurcation
When I was here talking in 2010, I showed this slide:

## Slide 37: Context: Bifurcating Analog Space
CHEAP analog
  Need the function, cheap
  Don’t need big SOC integration
  Don’t need 10M gates of logic
PRO
  Cheap, fewer nm effects
CON
  Can’t integrate lots of gates
AGGRESSIVE analog
  Need function AND integration
  Essential for lowest-power and highest-volume parts
PRO
  Power, access to 50M+ gates
CON
  Nanometer grief is worse here
-
+
Different kinds of design
problems driving a SPLIT

## Slide 38: TODAY’S Bifurcating Analog Space
2001
2005
2010
2015
2020
130nm
90nm
65nm
45nm
32nm
22nm
14nm
10nm
7nm
5nm
Today, most CHEAP ANALOG is
moving rapidly toward whatever
is the LAST PLANAR CMOS NODE
~28nm
AGGRESSIVE
analog in 14nm
 10nm
WHY?
Cheap analog
Aggressive analog
2010

## Slide 39: TODAY’S Bifurcating Analog Space
2001
2005
2010
2015
2020
130nm
90nm
65nm
45nm
32nm
22nm
14nm
10nm
7nm
5nm
CHEAP
AGGRESSIVE …….NEXT
LOW
POWER
CONNECTIVITY, MOBILITY,
INTERNET-OF-THINGS…
==

## Slide 40: TODAY’S Analog CAD Opportunities
2001
2005
2010
2015
2020
130nm
90nm
65nm
45nm
32nm
22nm
14nm
10nm
7nm
5nm
CHEAP
AGGRESSIVE …….NEXT
LAST PLANAR NODE CMOS
Old problems: Worse
Grand challenge: Aesthetics
NEW NON-PLANAR NODES
New problems: Many
Grand challenge: FinFets

## Slide 41: “Aesthetics Grand Challenge” for Layout
Allow layout designers to communicate geometric intent quickly and accurately, and use this to drive automatic layouts…
  (1) Obtained Easy+Fast (interactive, real-time)
  (2) Appear Trustworthy (exactly match designer’s aesthetics)
Think:
Floorplanning

## Slide 42: ‘Corollary’ Challenge
What layout happens in generators? What in place/route?
Hint: At final CMOS nodes, interesting action in both
GEN
PLACE & ROUTE

## Slide 43: The FinFet Challenge
Devices are radically different, dominated by litho regularity
Interconnect stack also different, very fine pitch for lower Metals
Source: Jan et al, “A 22nm SOC platform technology featuring 3-D tr-gate and high-k/metal gate, optimized for ultra low power, high performance and high density SOC applications,”, Prof IEEE IEDM, 2012.
Source: R. Borkar, N. Bohr, S. Jourdan, Advancing Moore’s Law on 2014. Aug 11, 2014. Intel Corp.

## Slide 44: FinFet Consequence: Placement
Custom analog cells look like row-based layout…
fin
gate
diffusion
DUMMY DEVICES, ON ALL SIDES
ACTIVE DEVICES
DUMMY
ACTIVE
ACTIVE
Strict matching rules (dummies)
Strict density rules (FEOL, MEOL)
Strict gradient rules for transition
Hard to do this by hand…
Source: R. Borkar, N. Bohr, S. Jourdan, Advancing Moore’s Law on 2014. Aug 11, 2014. Intel Corp.
fin
fin
fin
fin
fin

## Slide 45: FinFet Consequence: Routing
Lower metals very resistive (narrow) – can’t use for all signals
Intra-cell routing up stack to cross cell (like ASICs…)
DUMMY
ACTIVE
DUMMY
ACTIVE
ACTIVE
Source: Jan et al, “A 22nm SOC platform technology featuring 3-D tr-gate and high-k/metal gate, optimized for ultra low power, high performance and high density SOC applications,”, Prof IEEE IEDM, 2012.
??

## Slide 46: FinFet Problems for Analog Layout
Electromigration
  Analog wires carry big current
  Sizing/tapering to meet rules
Self-heating
  Wide (parallel) dev’s w/ current
  Result: hot device problems
Signal and power routing
  Many wires w/ varying currents
  Sizing not just EM, also DC drop
Coloring, multi-exposure litho
  Difficult for analog too
  Worse: more custom design here
Geometrically, electrically
challenging to do RIGHT

## Slide 47: FinFet Upside (Sort of…) for Analog CAD
2001
2005
2010
2015
2020
130nm
90nm
65nm
45nm
32nm
22nm
14nm
10nm
7nm
5nm
CHEAP
AGGRESSIVE …….NEXT
Circuit Designer
Layout Designer
Circuit Designer
Layout Designer

## Slide 48: Summary
Looking backward: Analog tools
  CAD= Optimization + constraints
  Learned: aesthetics & usage matter
  Many successes ….
Looking ahead: Analog Tools
  Analog essential for power/mobile
  Time to take fresh look at aesthetics
  FinFet: so different, so painful
  Great opportunities ahead for PD