## Slide 1
Po-Hsun Wu*, Mark Po-Hung Lin**, Xin Li***, and Tsung-Yi Ho****
*Dept. of CSIE, National Cheng Kung University, Tainan, Taiwan
** Dept. of EE, National Chung Cheng University, Chiayi, Taiwan
*** Dept. of ECE, Carnegie Mellon University, Pittsburgh, PA, USA
**** Dept. of CS, National Chiao Tung University, Hsinchu, Taiwan
ACM International Symposium on Physical Design 2015
Common-Centroid FinFET Placement
Considering the Impact of Gate Misalignment

## Slide 2: Outline
Introduction
Problem Formulation
Preliminary
Current Mismatch due to Gate Misalignment
Common-Centroid FinFET Placement Algorithms
Experimental Results
Conclusions

## Slide 3: Introduction
[23] A rigorous simulation based study of gate misalignment effects in gate engineered
double-gate (DG) MOSFETs [Sarangia et al., Superlattices Microstruct.’13]
Short channel effect
  Circuit performance, power dissipation, and reliability of circuits
New device technologies for circuit reliability improvement
Fin Field Effect Transistor (FinFET)
  Three-dimensional (3-D) structure
  Less leakage current
  Less threshold voltage variation
  Analog circuit application
Some lithography-induced process variations, such as gate misalignment, become more severe [23]
Source: Intel Corporation

## Slide 4: Gate Misalignment
-5
0
5
10
-10
(nm)
(a)
Gate
Source
Drain
(b)
Source
Drain
-5
0
5
10
-10
(nm)
: Expected position of the printed gate
: The printed gate with drain-side misalignment
: The printed gate with source-side misalignment
A FinFET without gate misalignment (Figure (a)):
  Ideal situation
A real FinFET with gate misalignment (Figure (b)):
  The misaligned distance can be as large as 5nm [Valin et al., TED’12]
  Threshold voltage increase and drain current decrease
  Current mirror and differential pair

## Slide 5: Analog Related Works
Common-centroid transistor placement
  [Lin et al., DAC’09], [Lin et al., TCAD’11], [Long et al., ISCAS’05]
  [Ma et al., TCAD’11], [Ma et al., ICCAD’07], [Xiao et al., ASPDAC’09],
  [Yan et al., ISVLSI’06], and [Zhang et al., ICCCAS’10]
  General common-centroid rules including coincidence, symmetry, dispersion, and compactness
  However, none of them considered the impact of gate misalignment
  Chirality condition of transistors [Long et al., ISCAS’05]
Common-centroid capacitor placement
  [Huang et al., TODAES’13], [Li et al., TCAD’14], [Lin et al., ICCAD’12]
  [Lin et al., TCAD’12], [Lin et al., TCAD’13], and [Lin et al., DAC’14]
  These works are still not associated with the FinFET technology

## Slide 6: Our Contribution
In this paper, we propose the novel common-centroid FinFET placement flow and algorithms
Our contributions can be summarized as follows:
  Consider the impact of gate misalignment and dispersion for next generation analog circuit design
  Derive a new quality metric for evaluating the matching quality of a current mirror
  Achieve much better current matching among transistors in a current mirror while maintaining high dispersion degree

## Slide 7
Introduction
Problem Formulation
Preliminary
Current Mismatch due to Gate Misalignment
Common-Centroid FinFET Placement Algorithms
Experimental Results
Conclusions

## Slide 8: Problem Formulation
Input: A netlist containing a set of sub-transistors of n FinFETs and general common-centroid rules
Objective: Determine the positions and orientations of all sub-transistors while minimizing the current mismatch, minimizing total placement area, and maximizing the dispersion degree
Constraint: Satisfy general common-centroid rules
*4- | -3* | *2- | -4*
-1* | -4* | *4- | -3*
*3- | -4* | *4- | *1-
*4- | -2* | *3- | -4*

## Slide 9
Introduction
Problem Formulation
Preliminary
  Current Mirror
  Circuit Mismatch
  Spatial Correlation Model
Current Mismatch due to Gate Misalignment
Common-Centroid FinFET Placement Algorithms
Experimental Results
Conclusions

## Slide 10: Current Mirror
Produce a constant replicated current, ICopy, of a scaled transistor, TS, by copying the reference current, IRef, of a reference transistor, TR
  W TS = n  W TR, ICopy = n  Iref
A current mirror may have several replicated currents with different scaling factors
TR
TS
IRef
ICopy
(a) A current mirror

## Slide 11: Circuit Mismatch
Matching quality optimization of a current mirror
The circuit mismatch occurs due to process variation [10]
  Systematic mismatch
  Random mismatch
To reduce systematic mismatch
  Divide all transistors into several
  smaller and identical sub-transistors
  Place them symmetrically with
  respect to a common center point
To reduce random mismatch
  Distribute all sub-transistors throughout a placement
  Exhibit the highest degree of dispersion
  Measure the dispersion degree by the spatial correlation model [10]
[10] Mismatch-aware common-centroid placement for arbitrary-ratio
capacitor arrays considering dummy capacitors [Lin et al., TCAD’12]
M1
D
S
M2
D
M2
D
S
M1
D
: Gate : Fin
: Diffusion : Metal
  : Common center point
(a)

## Slide 12: Spatial Correlation Model
Assume that all sub-transistors are arranged in an r × c matrix
For any two sub-transistors, sti and stj, located at the entries in the rith row and cith column and the rjth row and cjth column, their correlation coefficient ρij
where ρu = 0.9 and l = 1 [17]
For n transistors, the dispersion degree L
(1)
(2)
[17] Impact of capacitance correlation on yield enhancement of
mixed-signal/analog integrated circuits [Luo et al., TCAD’08]

## Slide 13
Introduction
Problem Formulation
Preliminary
Current Mismatch due to Gate Misalignment
  Evaluation of Current Mismatch
  A Case Study
Common-Centroid FinFET Placement Algorithms
Experimental Results
Conclusions

## Slide 14: Evaluation of Current Mismatch (1/3)
Drain current variation due to the gate misalignment
Evaluate the current mismatch of a current mirror with the impact of gate misalignment
Given a set of k transistors and each transistor, ti, contains ni sub-transistors with determined orientations
Based on the multiplication property of equality
(4)
(3)

## Slide 15: Evaluation of Current Mismatch (2/3)
(5)
After splitting the Equation (4), we can obtain a set of k(k-1) equalities

## Slide 16: Evaluation of Current Mismatch (3/3)
By substituting ni = nid+nis into Equation (5) and simplifying the resulting equalities
Derive the overall current mismatch by summing up all
(7)
(6)

## Slide 17: A Case Study
(c)
(d)
*2- | -3* | *4- | -4*
-3* | *4- | -4* | *1-
-1* | *4- | -4* | *3-
-4* | *4- | -3* | *2-
(b)
*3- | -4* | *2- | -4*
-4* | *3- | -4* | *1-
-1* | *4- | -3* | *4-
-4* | *2- | -4* | *3-
*4- | -3* | *2- | -4*
-1* | -4* | *4- | -3*
*3- | -4* | *4- | *1-
*4- | -2* | *3- | -4*
*: Drain -: Source
(a)
Placements | # of Sub-transistors | Simulated Current Ratio | ϵ | L
Figure (b) | 2, 2, 4, 8 | 1.00 : 0.93 : 2.07 : 4.00 | 0.16 | 5.6827
Figure (c) |  | 1.00 : 0.93 : 1.93 : 4.14 | 0.17 | 5.7338
Figure (d) |  | 1.00 : 1.00 : 2.00 : 4.00 | 0.00 | 5.7459
Table 1: Comparisons of the simulated current ratios, current mismatch (ϵ) and dispersion degree (L) for different common-centroid placements in (b)–(d).
Estimate the drain current of each transistor based on the BSIM-CMG model [15]
[15] BSIM 3v3.2 MOSFET model users' manual [Liu et al., Technical Report’98]
M1
M2
M3
M4
IRef
I2
I3
I4

## Slide 18
Introduction
Problem Formulation
Preliminary
Current Mismatch due to Gate Misalignment
Common-Centroid FinFET Placement Algorithms
  Determination of Sub-transistor Orientations
    Minimum-weight Clique Model
  Common-Centroid FinFET Placement Considering Dispersion and Diffusion Sharing
  Dispersion Degree Maximization
Experimental Results
Conclusions

## Slide 19: Determination of Sub-transistor Orientations
Enumerate all configurations of sub-transistor orientations
A k-finger FinFET has k+1 configurations
Minimum-weight Clique Problem
A
S
D
A
S
D
A
S
D
Configuration 1
3 drain-side misalignment
0 source-side misalignment
A
S
D
A
S
D
A
S
D
Configuration 2
2 drain-side misalignment
1 source-side misalignment
A
S
D
A
S
D
A
S
D
Configuration 3
1 drain-side misalignment
2 source-side misalignment
A
S
D
A
S
D
A
S
D
Configuration 4
0 drain-side misalignment
3 source-side misalignment
(a)
(b)
(c)
(d)

## Slide 20: Minimum-weight Clique Problem [3]
A1-C2
nC1s, nC1d
nC3s, nC3d
nB1s, nB1d
nA2s, nA2d
nC2s, nC2d
nA1s, nA1d
A1-C1
A1-C3
A2-C1
A2-C2
A2-C3
B1-C1
B1-C2
A2-B1
A1-B1
nB2s, nB2d
A2-B2
A1-B2
B2-C3
B2-C2
B2-C1
[3] Introduction to Algorithms [Cormen, McGraw-Hill’01]
nis: nis sub-transistors with source-side misalignment
nid: nid sub-transistors with drain-side misalignment
ti-tj: the current mismatch between ti and tj

## Slide 21
Introduction
Problem Formulation
Preliminary
Current Mismatch due to Gate Misalignment
Common-Centroid FinFET Placement Algorithms
  Determination of Sub-transistor Orientations
  Common-Centroid FinFET Placement Considering Dispersion and Diffusion Sharing
    Euler Path
    Dispersion Degree Maximization during Searching the Euler Path
  Dispersion Degree Maximization
Experimental Results
Conclusions

## Slide 22: Common-Centroid FinFET Placement Considering Dispersion and Diffusion Sharing
The sub-transistors in (m - i + 1)th row are symmetrical to that in ith row for an m-row placement
Find the representative transistors of each transistor
Distribute all representative transistors of each transistor, ti, to different rows
  The number of representative transistors of ti is greater than
    Evenly distribute these representative transistors
  The number of representative transistors of ti is less than
    Randomly assign these representative transistors
(a)
*1-
-2*
-3*
*3-
-4*
*4-
-4*
*4-
-5*
*5-
-5*
*5-
-5*
*5-
-5*
*5-
*1-
-4*
*3-
(b)
*4-
*5-
*5-
-5*
-5*
*: Source
-: Drain

## Slide 23: Euler Path
Construct the diffusion graph and find the Euler path [20] to generate the respective placement for each row
Two representative transistors are called unrelated transistors if they belong to different transistors
Two representative transistors are called related transistors if they belong to the same transistor
[20] Automated hierarchical CMOS analog circuit stack generation with intramodule connectivity and matching considerations [Naiknaware et al., JSSC’99]
(a)
(b)
-1*
*3-
*2-
-2*
*3-
-3*
*i-: Gate misalignment
from Source to Drain
-i*: Gate misalignment
from Drain to Source
: Transistor 1
: Transistor 2
: Transistor 3
: Drain terminal
: Source terminal
D
S
D
S

## Slide 24: Dispersion Degree Maximization during Searching the Euler Path
To maximize the dispersion degree
  Maximize
    Minimize the distance of unrelated transistors
  Minimize
    Maximize the distance of related transistors
Repeat the above steps for each row and produce the symmetrical row
(2)
(b)
(1)
-1*
*3-
*2-
-2*
*3-
-3*
*: Source
-: Drain
(a)
D
S
: Transistor 1
: Transistor 2
: Transistor 3

## Slide 25
Introduction
Problem Formulation
Preliminary
Current Mismatch due to Gate Misalignment
Common-Centroid FinFET Placement Algorithms
  Determination of Sub-transistor Orientations
  Common-Centroid FinFET Placement Considering Dispersion and Diffusion Sharing
  Dispersion Degree Maximization
    Shortest Path Problem
Experimental Results
Conclusions

## Slide 26: Dispersion Degree Maximization
Adjust the relative positions of different sub-transistors among different rows
Placement rotation
  Iteratively move the sub-transistor at the end of the row to the beginning of the row
The simultaneous selection of the best placement of different rows is formulated as the shortest path problem
(a) Initial placement
(c) Derivation 2
-4* | *4- | -3* | *2-
*4- | -3* | *2- | -4*
*2- | -4* | *4- | -3*
-3* | *2- | -4* | *4-
(b) Derivation 1
(d) Derivation 3

## Slide 27: Shortest Path Problem
Each row is represented by a group node
Each possible placement is denoted by an element node
The weight of each edge between two element nodes is the dispersion degree
Rij
: Element node
: Group node
Weight
0
0
0
Ri1Ri+11
Ri+12
Ri+1k
Rm1
Rm2
Rmk
0
0
0
Ri1
Ri2
Rik
R11
R12
R1k
Ri+11
.
.
.
.
.
.
.
.
.
.
.
.
T
S

## Slide 28
Introduction
Problem Formulation
Preliminary
Current Mismatch due to Gate Misalignment
Common-Centroid FinFET Placement Algorithms
Experimental Results
  Experimental Setup
  Numerical Comparisons
Conclusions

## Slide 29: Experimental Setup
Implemented our algorithm in MATLAB language on a 3.4 GHz Windows machine with 16GB memory
Comparison
  [14] Thermal-driven analog placement considering device matching [Lin et al., TCAD’11]
  Without gate misalignment
Tested on a set of current mirrors with different width ratios of the scaled transistors
Testcases | # of Sub-transistors
CM1 | 1, 1
CM2 | 1, 1, 2
CM3 | 1, 1, 2, 4
CM4 | 1, 1, 2, 4, 8
CM5 | 1, 1, 2, 4, 8, 16
CM6 | 1, 1, 2, 4, 8, 16, 32
CM7 | 1, 1, 2, 4, 8, 16, 32, 64
CM8 | 1, 1 ,2, 4, 8, 16, 32, 64, 128
Table 2: Benchmark statistics.

## Slide 30: Numerical Comparisons
Test Cases | Lin et al.’s approach [14] |  |  | Our approach |  |  | Comparison (%) | 
 | Simulated Current Ratio | ϵ / L | Time (s) | Simulated Current Ratio | ϵ / L | Time (s) | ϵ / L | Time
CM1 | 1:0.93 | 0.07/0.90 | 0.01 | 1:1 | 0.00/0.90 | 0.01 | -100/0.00 | 0.00
CM2 | 1:1:1.85 | 0.14/2.73 | 0.02 | 1:1:2 | 0.00/2.73 | 0.02 | -100/0.00 | 0.00
CM3 | 1:1:1.85:3.92 | 0.22/5.55 | 0.03 | 1:1:1.93:3.86 | 0.12/5.58 | 0.04 | -46.14/0.61 | 33.10
CM4 | 1:1:1.85:3.92:4.00 | 0.35/9.19 | 0.04 | 1:1:1.93:3.93:7.63 | 0.24/9.48 | 0.05 | -30.00/3.18 | 25.13
CM5 | 1:1:1.85:3.77:8.00: 15.11 | 0.41/13.69 | 0.07 | 1:1:1.93:3.86:7.78: 15.48 | 0.28/14.23 | 0.11 | -32.29/3.94 | 71.45
CM6 | 1:0.93:1.92:3.85 :7.48: 15.11 : 31.26 | 0.41/13.69 | 0.20 | 1:1:1.93:3.93:7.63: 15.33:30.89 | 0.45/19.91 | 0.55 | -25.72/4.31 | 180.87
CM7 | 1:1:1.85:3.85:7.92: 15.63 : 31.11 : 60.95 | 0.79/25.23 | 0.75 | 1:1:1.93:3.86:7.71: 15.26 :30.81:61.77 | 0.48/26.36 | 3.38 | -38.83/4.47 | 351.26
CM8 | 1:0.93:1.85:3.85:7.55: 15.48:31.26:61.77:122.70 | 0.93/32.13 | 3.44 | 1:1:1.93:3.86:7.71: 15.48:30.96:61.92:122.60 | 0.54/33.62 | 5.10 | -41.86/4.63 | 48.19
Table 3: Comparisons of simulated current ratios, current mismatch (ϵ), and dispersion degree (L), based on Lin et al.’s and our approaches.

## Slide 31: Generated Placement of CM8
The resulting common-centroid FinFET placements of CM8. (a) The placement generated by Lin et al.’s approach.
(b) The placement generated by our approach.
*: Drain -: Source

## Slide 32
Introduction
Problem Formulation
Preliminary
Current Mismatch due to Gate Misalignment
Common-Centroid FinFET Placement Algorithms
Experimental Results
Conclusions

## Slide 33: Conclusions
In this paper, we have introduced the impact of gate misalignment to the drain current of different common-centroid FinFET placements
We have proposed a novel placement flow and algorithms to generate the common-centroid FinFET placements while considering the impact of gate misalignment and dispersion
Experimental results have shown that the proposed algorithms can effectively reduce the impact of gate misalignment to the drain current and maximize the dispersion degree of a common-centroid FinFET placement

## Slide 34
Thank You for
Your Attention!