## Slide 1: Q-Learning Based Dynamic Voltage Scaling for Designs with Graceful Degradation
Yu-Guang Chen1,2, Wan-Yu Wen1, Tao Wang2,
Yiyu Shi2, and Shih-Chieh Chang1
1Department of CS, National Tsing Hua University, HsinChu, Taiwan
2Department of ECE, Missouri University of Science and Technology, Rolla, Mo, USA
Notes: Ladies and gentlemen, good morning. The topic of today’s talk is “Critical Path Monitor Enabled Dynamic Voltage Scaling for Graceful Degradation in Sub-Threshold Designs.”
I am Yu-Guang Chen from National Tsing Hua University, Hsinchu, Taiwan.
This is a joint work with my friends Tao Wang, Kuan-Yu Lai, Wan-Yu Wen, and Prof. Yiyu Shi from Missouri University of Science and Technology, USA. And my advisior Shih-Chieh Chang from National Tsing Hua University, Hsinchu Taiwan.
The motivation of this work is as follows.

## Slide 2: Outline
Introduction and Motivation
Q-Learning Based DVS Scheme
Experimental Results
Conclusions

## Slide 3: Outline
Introduction and Motivation
Q-Learning Based DVS Scheme
Experimental Results
Conclusions

## Slide 4: Introduction and Motivation
Power consumption is an significant problem in modern IC designs.
Dynamic voltage scaling (DVS) can efficiently reduce operating power.
  Dynamically switch operating voltage and/or operating frequency
  Workload, Process, Environment variations

## Slide 5: Introduction and Motivation
The key concept of DVS is to decide the optimal operating voltage for different scenarios.
Deterministic DVS schemes
  Construct state table off-line on various statistical analysis.
  Optimal voltage comes from the real-time feedback and the state table.

## Slide 6: Introduction and Motivation
Hard for two reasons:
  Many uncertainties are non-Gaussian and tightly correlated;
  Much information may not be known a priori.
Reinforcement learning based DVS schemes
  Dynamically adjust the policy at runtime based on the system performance
  through various learning procedures

## Slide 7: Introduction and Motivation
Graceful degradation
  Allow timing errors to occur with a low probability
  Significantly reduce operating power
  Timing Error Probability (TEP)
  Only a few prior works consider DVS with Graceful degradation

## Slide 8: Introduction and Motivation
Critical Path Monitor (CPM)
  Measures critical path delays
  Reflects the influence of process and temperature variations dynamically

## Slide 9: Introduction and Motivation
Motivation example
  Deterministic joint probability density function (JPDF) based DVS scheme for graceful degradation
  Calls for learning based DVS schemes

## Slide 10: Problem Formulation
Given
  A chip with CPM placed,
  the voltage candidates for DVS, and
  a TEP bound and a timing window length for TEP measurement,
Determine
  The optimal operating voltages at runtime based on the sampled slack from the CPM
Goal
  The operating power is minimized.

## Slide 11: Outline
Introduction and Motivation
Q-Learning Based DVS Scheme
Experimental Result
Conclusions

## Slide 12: Framework
Construct 2D state table
  Row  particular operating voltage candidate
  Column  particular reading from the CPM
  Score  corresponding combination of operating voltage and sampled slack from CPM
Voltage\Slack | 0.1ns | 0.2ns | 0.3ns | … | 1.0ns
0.8V | 1 | 2 | 5 | … | 10
0.9V | 4 | 3 | 8 | … | 8
1.0V | 8 | 10 | 10 | … | 4
1.1V | 10 | 8 | 8 | … | 2
1.2V | 3 | 5 | 4 | … | 1

## Slide 13: Framework
Optimal operating voltage decision
  DVS controller samples the slack from the CPM
  Identifies the voltage candidate with the highest score in the corresponding column
  Change the operating voltage
Voltage\Slack | 0.1ns | 0.2ns | 0.3ns | … | 1.0ns
0.8V | 1 | 2 | 5 | … | 10
0.9V | 4 | 3 | 8 | … | 8
1.0V | 8 | 10 | 10 | … | 4
1.1V | 10 | 8 | 8 | … | 2
1.2V | 3 | 5 | 4 | … | 1

## Slide 14: Framework
Optimal operating voltage decision
  DVS controller samples the slack from the CPM
  Identifies the voltage candidate with the highest score in the corresponding column
  Change the operating voltage
Voltage\Slack | 0.1ns | 0.2ns | 0.3ns | … | 1.0ns
0.8V | 1 | 2 | 5 | … | 10
0.9V | 4 | 3 | 8 | … | 8
1.0V | 8 | 10 | 10 | … | 4
1.1V | 10 | 8 | 8 | … | 2
1.2V | 3 | 5 | 4 | … | 1

## Slide 15: Framework
Optimal operating voltage decision
  DVS controller samples the slack from the CPM
  Identifies the voltage candidate with the highest score in the corresponding column
  Change the operating voltage
Voltage\Slack | 0.1ns | 0.2ns | 0.3ns | … | 1.0ns
0.8V | 1 | 2 | 5 | … | 10
0.9V | 4 | 3 | 8 | … | 8
1.0V | 8 | 10 | 10 | … | 4
1.1V | 10 | 8 | 8 | … | 2
1.2V | 3 | 5 | 4 | … | 1

## Slide 16: Framework
Optimal operating voltage decision
  DVS controller samples the slack from the CPM
  Identifies the voltage candidate with the highest score in the corresponding column
  Change the operating voltage
Voltage\Slack | 0.1ns | 0.2ns | 0.3ns | … | 1.0ns
0.8V | 1 | 2 | 5 | … | 10
0.9V | 4 | 3 | 8 | … | 8
1.0V | 8 | 10 | 10 | … | 4
1.1V | 10 | 8 | 8 | … | 2
1.2V | 3 | 5 | 4 | … | 1

## Slide 17: Framework
Optimal operating voltage decision
  DVS controller samples the slack from the CPM
  Identifies the voltage candidate with the highest score in the corresponding column
  Change the operating voltage
Voltage\Slack | 0.1ns | 0.2ns | 0.3ns | … | 1.0ns
0.8V | 1 | 2 | 5 | … | 10
0.9V | 4 | 3 | 8 | … | 8
1.0V | 8 | 10 | 10 | … | 4
1.1V | 10 | 8 | 8 | … | 2
1.2V | 3 | 5 | 4 | … | 1

## Slide 18: Q-learning
Applies to Markov decision problems with unknown costs and transition probabilities.
State
  A legal status
Action
  A legal transition from one state to another
Q-table
  Store Q-values for each state-action pair
  Expected pay-off from choosing the given action from that state
  Are updated through reward and penalty policies

## Slide 19: Q-learning Based DVS Scheme
State
  A combination of an operating voltage and a sampled slack.
Action
  A voltage transition under the same sampled slack.
Q-table
  Store Q-values from changing the operating voltage under the same sampled slack.

## Slide 20: Q-learning Based DVS Scheme
Reward
  State as operating voltage and sampled slack
  Action = () as voltage scaling from to
  Entry of Q-table as Q-value for switching from to state (take action )
  is the power reduction from action

## Slide 21: Q-learning Based DVS Scheme
Penalty
  Prevent TEP() from exceeding the TEP bound().
  Abrupt penalty
    Constant and large penalty
  Linearly graded penalty
    Linearly increase the penalty

## Slide 22: Q-learning Based DVS Scheme
Penalty as the penalty of
  Abrupt penalty
  ε is a small constant
  ρ is a small positive constant set as a margin
  is a constant

## Slide 23: Q-learning Based DVS Scheme
Linearly graded penalty
)
  γ is grading factor.

## Slide 24: Q-learning Based DVS Scheme
Q-values update policy
  denotes the learning rate
  P is defined as
  is the sampled slack after voltage scaling

## Slide 25: Q-learning Based DVS Scheme
Summarize
  Step 1: When the Q-learning process starts, initialize all the Q-values in the Q-table to 0.
  Step 2: Denote the current state as . Find an action with the highest Qjk for all the eligible j’s. Switch to .
  Step 3: Evaluate and update TEP. Calculate the corresponding reward and penalty .Then update Qik.
  Step 4: Set the current state as , and go to Step.2 when the next cycle starts.

## Slide 26: Outline
Introduction and Motivation
Q-Learning Based DVS Scheme
Experimental Result
Conclusions

## Slide 27: Experimental Results
Three industrial designs with 45nm library
8-core, 2.40GHZ, Intel Xeon E5620 CPU, with 32GB memory, CentOS release 5.9 machine
Voltage candidates are set to 0.8V, 0.9V, 1V, 1.1V, 1.2V
Temperature varies from 20oC to 35oC.

## Slide 28: Experimental Results
Performance
  stepping based
  JPDF based
  Power is in µW

## Slide 29: Experimental Results
Performance
  stepping based
  JPDF based
  Power is in µW

## Slide 30: Experimental Results
Different TEP bounds v.s. TPE achieved

## Slide 31: Experimental Results

## Slide 32: Outline
Introduction and Motivation
Q-Learning Based DVS Scheme
Experimental Result
Conclusions

## Slide 33: Conclusions
We have proposed a Q-learning based DVS scheme dedicated to the designs with graceful degradation.
Proposed Q-learning based scheme can achieve up to 83.9% and 29.1% power reduction respectively with 0.01 TEP bound.

## Slide 34: Thank You Q&A
Notes: Thanks a lot for your attention.
If you are interesting in this work, plz come to my booth after this section and I can bring more details about this work.

## Slide 36: Experimental Results
Impact of the penalty functions

## Slide 37: Experimental Results
Learning rate α and the power reduction

## Slide 38: Experimental Results
Noise v.s. power reduction and TEP achieved.