## Slide 1
Machine Learning in Simulation-Based Analysis
Li-C. Wang,
Malgorzata Marek-Sadowska
University of California, Santa Barbara

## Slide 2: Synopsis
Simulation is a popular approach employed in many EDA applications
In this work, we explore the potential of using machine learning to improve simulation efficiency
While the work is developed based on specific simulation contexts, the concepts and ideas should be applicable to a generic simulation setting

## Slide 3
Problem Setting

## Slide 4: Problem Setting
Inputs to the simulation
  X: e.g. input vectors, waveforms, assembly programs, etc.
  C: e.g. device parameters to model statistical variations
Output from the simulation:
  Y: e.g. output vectors, waveforms, coverage points
Goal of simulation analysis: To analyze the behavior of the mapping function f()
Mapping Function f( )
(Design Under Analysis)
Component random variables
Input random
variables
Output
behavior
X
C
Y

## Slide 5: Practical View of The Problem
For the analysis task, k essential outputs are enough
  k << n*m
Fundamental problem:
  Before simulation, how can we predict the inputs that will generate the essential outputs?
f( )
Checker
How to predict the outcome of
an input before its simulation?
Essential outputs

## Slide 6: First Idea: Iterative Learning
Learning objective: to produce a learning model that predicts the “importance of an input”
l input
samples
Learning &
Selection
h potentially
important
input samples
Simulation
Checker
outputs
results
Results include 2 types of information:
Inputs that do not produce essential outputs
Inputs that do produce essential outputs

## Slide 7
Machine Learning Concepts

## Slide 8: For More Information
Tutorial on Data Mining in EDA & Test
  IEEE CEDA Austin chapter tutorial – April 2014
  http://mtv.ece.ucsb.edu/licwang/PDF/CEDA-Tutorial-April-2014.pdf
Tutorial papers
  “Data Mining in EDA” – DAC 2014
    Overview and include a list of references to our prior works
  “Data Mining in Functional Debug” – ICCAD 2014
  “Data Mining in Functional Test Content Optimization” – ASP DAC 2015

## Slide 9: How A Learning Tool Sees The Data
A learning algorithm usually sees the dataset as above
  Samples: examples to be reasoned on
  Features: aspects to describe a sample
  Vectors: resulting vector representing a sample
  Labels: care behavior to be learned from (optional)
features
samples
labels
vectors

## Slide 10: Supervised Learning
Classification
  Labels represent classes (e.g. +1, -1: binary classes)
Regression
  Labels are some numerical values (e.g. frequencies)
(features)
Labels

## Slide 11: Unsupervised Learning
Work on features
  Transformation
  Dimension reduction
Work on samples
  Clustering
  Novelty detection
  Density estimation
(features)
No y’s

## Slide 12: Semi-Supervised Learning
Only have labels for i samples
  For i << m
Can be solved as an unsupervised problem with supervised constraints
(features)
Labels for i samples only

## Slide 13: Fundamental Question
A learning tool takes data as a matrix
Suppose we want to analyze m samples
  waveforms, assembly programs, layout objects, etc.
How do I feed the samples to the tool?
Learning tool
Sample 1
Sample 2
…
Sample m
?
Matrix view

## Slide 14: Explicit Approach – Feature Encoding
Need to develop two things:
  1. Define a set of features
  2. Develop a parsing and encoding method based on the set of features
Does learning result then depend on the features and encoding method? (Yes!)
That’s why learning is all about “learning the features”
Samples
Parsing and
encoding method
Set of Features

## Slide 15: Implicit Approach – Kernel Based Learning
Define a similarity function (kernel function)
  It is a computer program that computes a similarity value between any two tests
Most of the learning algorithms can work with such a similarity function directly
  No need for a matrix data input
Sample i
Sample j
Similarity
Function
Similarity value

## Slide 16: Kernel-Based Learning
A kernel based learning algorithm does not operate on the samples
As long as you have a kernel, the samples to analyze
  Vector form is no longer needed
Does learning result depend on the kernel? (Yes!)
That’s why learning is about learning a good kernel
Kernel function
Learning
Algorithm
Learned model
Query for
pair (xi,xj)
Similarity Measure for (xi,xj)

## Slide 17
Example:
RTL Simulation Context

## Slide 18: Recall: Iterative Learning
Learning objective: to produce a learning model that predicts the “importance of an input”
l input
samples
Learning &
Selection
h potentially
important
input samples
Simulation
Checker
outputs
results
Results include 2 types of information:
Inputs that do not produce essential outputs
Inputs that do produce essential outputs

## Slide 19: Iterative Learning
Learning objective: to produce a learning model that predicts the “inputs likely to improve coverage”
l assembly
programs
Learning &
Selection
h potentially
important
assembly programs
Simulation
Checker
outputs
results
Results include 2 types of information:
Inputs that provide no new coverage
Inputs that provide new coverage

## Slide 20: Unsupervised: Novelty Detection
Learning is to model the simulated assembly programs
Use the model to identify novel assembly programs
A novel assembly program is likely to produce new coverage
: simulated assembly programs
: filtered assembly programs
: novel assembly programs
Boundary captured by a one-class learning model

## Slide 21: One Example
Design: 64-bit Dual-thread low-power processor (Power Architecture)
Each test is with 50 generated instructions
Roughly saving: 94%
Chart: # of applied tests
With novelty detection, only 100 tests are needed
Without novelty detection, 1690 tests are needed

## Slide 22: Another Example
Each test is a 50-instruction assembly program
Tests target on Complex FPU (33 instruction types)
Roughly saving: 95%
  Simulation is carried out in parallel in a server farm
Chart: # of applied tests
Series 2 | 33168 | 34541 | 34541 | 34557 | 34557
19+ hours simulation
With novelty detection
=> Require only 310 tests
Without novelty detection
=> Require 6010 tests

## Slide 23
Example:
SPICE Simulation Context
(Include C Variations)

## Slide 24: SPICE Simulation Context
Mapping function f()
  SPICE simulation of a transistor netlist
Inputs to the simulation
  X: Input waveforms over a fixed period
  C: Transistor size variations
Output from the function: Y – output waveforms
Mapping Function f( )
Design Under Analysis
Transistor size variations
X
C
Y
Chart: 
 | 0.02856 | 1.125 | 0.01108 | 1.185 | 0.01474 | 1.199 | 0.007791 | 1.188 | 0.009136 | 1.141 | 0.02775 | 0.9555 | 0.131 | 0.6852 | 0.3082 | 0.4074 | 0.5438 | 0.1004 | 0.8658 | 0.03791 | 1.033 | 0.01901 | 1.148 | 0.01955 | 1.178 | 0.009437 | 1.2 | 0.01201 | 1.204 | 0.006861 | 1.166 | 0.009273 | 1.119 | 0.04707 | 0.9367 | 0.1115 | 0.7073 | 0.281 | 0.463 | 0.4746 | 0.1523 | 0.7469 | 0.06669 | 0.9445 | 0.02474 | 1.064 | 0.02273 | 1.143 | 0.01072 | 1.187
Chart: 
 | 0.1607 | 1.209 | 0.02459 | 0.385 | 1.18 | 0.01227 | 0.654 | 1.121 | 0.01317 | 0.7904 | 1.041 | 0.009176 | 0.959 | 0.9762 | 0.01003 | 0.9468 | 0.9616 | 0.008522 | 0.9554 | 0.9793 | 0.01071 | 0.8267 | 1.084 | 0.01067 | 0.6774 | 1.162 | 0.01743 | 0.4506 | 1.193 | 0.01267 | 0.257 | 1.209 | 0.03669 | 0.104 | 1.215 | 0.09104 | 0.01936 | 1.203 | 0.3307 | 0.006739 | 1.171 | 0.4892 | 0.006919 | 1.127 | 0.7082 | 0.008104 | 1.074 | 0.797 | 0.007327 | 1.038
Chart: 
 | 1.197 | 0.0162 | 0.6363 | 0.8214 | 0.01043 | 1.219 | 0.009688 | 0.8726 | 0.5655 | 0.03384 | 1.217 | 0.009893 | 1.035 | 0.3237 | 0.07728 | 1.192 | 0.009837 | 1.135 | 0.1567 | 0.1621 | 1.144 | 0.008786 | 1.168 | 0.08328 | 0.276 | 1.094 | 0.00796 | 1.185 | 0.02785 | 0.3794 | 1.045 | 0.007567 | 1.187 | 0.03053 | 0.4422 | 0.9952 | 0.007355 | 1.193 | 0.02116 | 0.4732 | 0.974 | 0.007218 | 1.194 | 0.02027 | 0.48 | 0.9895 | 0.007295 | 1.192 | 0.01458 | 0.4523
Chart: 
 | -3.454e-06 | -4.545e-06 | 2.511e-05 | 0.9274 | 1.198 | 1.2 | 1.2 | 1.2 | 1.2 | 1.2 | 1.2 | 1.2 | 1.2 | 1.2 | 1.198 | 1.2 | 1.2 | 1.2 | 1.2 | 1.2 | 1.2 | 1.2 | 1.2 | 1.2 | 1.2 | 1.2 | 1.202 | 0.2368 | 0.0002793 | 3.13e-05 | 1.313e-05 | 1.212e-05 | 2.514e-05 | 3.689e-06 | 7.75e-06 | 7.009e-06 | 5.054e-06 | 2.351e-06 | 5.435e-06 | 0.001617 | -1.197e-05 | 0 | -1.232e-06 | 2.71e-06 | -5.887e-06 | 5.09e-07 | 3.329e-06 | -5.349e-06 | 1.858e-06 | 3.926e-06
Chart: 
 | 1.2 | 1.203 | 0.0811 | -0.0002205 | -8.218e-05 | -4.115e-05 | -2.56e-05 | -1.575e-05 | -1.999e-05 | 0.001429 | -2.254e-05 | -1.596e-05 | -7.925e-06 | -1.195e-05 | -1.021e-05 | -8.841e-06 | 0.0001823 | 1.04 | 1.199 | 1.2 | 1.2 | 1.2 | 1.2 | 1.2 | 1.198 | 1.2 | 1.2 | 1.2 | 1.2 | 1.2 | 1.2 | 1.2 | 1.22 | 0.006828 | 6.363e-05 | 2.306e-05 | 8.476e-06 | 7.733e-06 | 4.396e-06 | 2.547e-05 | 0.000411 | 5.62e-06 | 1.152e-05 | 1.298e-05 | -8.845e-07 | 2.076e-06 | -3.51e-06 | -0.004881 | 1.188 | 1.2
Chart: 
 | 6.955e-07 | 5.135e-06 | -1.848e-06 | 9.591e-07 | 2.374e-05 | 1.16 | 1.2 | 1.2 | 1.2 | 1.2 | 1.2 | 1.2 | 1.2 | 1.2 | 1.198 | 1.2 | 1.2 | 1.2 | 1.2 | 1.2 | 1.2 | 1.2 | 1.2 | 1.2 | 1.198 | -0.001657 | -0.0001609 | -7.161e-05 | -2.681e-05 | -3.553e-05 | -2.021e-05 | -1.551e-05 | -1.581e-05 | -4.168e-06 | 0.0008425 | -1.916e-05 | -1.456e-05 | -1.365e-05 | -2.184e-06 | -1.555e-05 | -4.16e-06 | -6.118e-06 | -6.338e-06 | -6.612e-06 | 0.09436 | 1.198 | 1.2 | 1.2 | 1.2 | 1.2

## Slide 25: Recall: Iterative Learning
In each iteration, we will learn a model to predict the inputs likely to generate additional essential output waveforms
l input
waveforms
Learning &
Selection
h potentially
important
waveforms
Simulation
Checker
outputs
results
Results include 2 types of information:
Inputs that do not produce essential outputs
Inputs that do produce essential outputs

## Slide 26: Illustration of Iterative Learning
i = 2
i = 1
For an important input, continue the search in the neighboring region
For an unimportant input, avoid the inputs in the neighboring region
s4
y4
s3
s1
s2
y3
y1
y2
s5
s6
y6
y5
?
i = 0
XC space
Y space

## Slide 27: Idea: Adaptive Similarity Space
In each iteration, similarity is measured in the space defined by important inputs
Instead of applying novelty detection, we apply clustering here to find “representative inputs”
s1
s2
s1
s2
Space implicitly defined by k( )
Adaptive similarity space
Three additional
samples selected

## Slide 28: Initial Result – UWB-PLL
We will perform 4 sets of the experiments – each set is for each input-output pair
I4
O4
I1
O1
I2
O2
I3
O3

## Slide 29: Initial Result
Comparing to random input selection
For each case, the # of essential outputs is shown
Learning enables simulation of less # of inputs to obtain the same coverage of the essential outputs

## Slide 30: Additional Result – Regulator
I
O1
O2
 |  | Apply Learning |  | Random | 
In | Out | # IS’s | #EO’s | # IS’s | #EO’s
I | O1 | 153 | 84 | 388 | 84
I | O2 | 107 | 49 | 355 | 49

## Slide 31: Coverage Progress
Chart: 
# of covered EI’s
# of applied tests
Regulator I - O1
With novelty detection
=> Require only 153 tests
Without novelty detection, 388 tests are needed
~60% cost reduction

## Slide 32: Additional Result – Low Power, Low Noise Amp.
I1
O1
 |  | Apply Learning |  | Random | 
In | Out | # IS’s | #EO’s | # IS’s | #EO’s
I1 | O1 | 96 | 75 | 615 | 75

## Slide 33: 2nd Idea: Supervised Learning Approach
In some applications, one may desire to predict the actual output (e.g. waveform) of an input (rather than just the importance of an input)
In this case, we need to apply a supervised learning approach (see paper for more detail)
input
samples
Learning model
Predictable?
yes
Predictor
Predicted
outputs
Simulation
no
Simulated outputs

## Slide 34: Recall: Supervised Learning
Fundamental challenge:
  Each y’s is a complex object (e.g. a waveform)
How do we build a supervised learning model in this case? (See the paper for discussion)
(features)
Waveforms
Chart: 
 | -3.454e-06 | -4.545e-06 | 2.511e-05 | 0.9274 | 1.198 | 1.2 | 1.2 | 1.2 | 1.2 | 1.2 | 1.2 | 1.2 | 1.2 | 1.2 | 1.198 | 1.2 | 1.2 | 1.2 | 1.2 | 1.2 | 1.2 | 1.2 | 1.2 | 1.2 | 1.2 | 1.2 | 1.202 | 0.2368 | 0.0002793 | 3.13e-05 | 1.313e-05 | 1.212e-05 | 2.514e-05 | 3.689e-06 | 7.75e-06 | 7.009e-06 | 5.054e-06 | 2.351e-06 | 5.435e-06 | 0.001617 | -1.197e-05 | 0 | -1.232e-06 | 2.71e-06 | -5.887e-06 | 5.09e-07 | 3.329e-06 | -5.349e-06 | 1.858e-06 | 3.926e-06
Chart: 
 | 1.2 | 1.203 | 0.0811 | -0.0002205 | -8.218e-05 | -4.115e-05 | -2.56e-05 | -1.575e-05 | -1.999e-05 | 0.001429 | -2.254e-05 | -1.596e-05 | -7.925e-06 | -1.195e-05 | -1.021e-05 | -8.841e-06 | 0.0001823 | 1.04 | 1.199 | 1.2 | 1.2 | 1.2 | 1.2 | 1.2 | 1.198 | 1.2 | 1.2 | 1.2 | 1.2 | 1.2 | 1.2 | 1.2 | 1.22 | 0.006828 | 6.363e-05 | 2.306e-05 | 8.476e-06 | 7.733e-06 | 4.396e-06 | 2.547e-05 | 0.000411 | 5.62e-06 | 1.152e-05 | 1.298e-05 | -8.845e-07 | 2.076e-06 | -3.51e-06 | -0.004881 | 1.188 | 1.2
Chart: 
 | 6.955e-07 | 5.135e-06 | -1.848e-06 | 9.591e-07 | 2.374e-05 | 1.16 | 1.2 | 1.2 | 1.2 | 1.2 | 1.2 | 1.2 | 1.2 | 1.2 | 1.198 | 1.2 | 1.2 | 1.2 | 1.2 | 1.2 | 1.2 | 1.2 | 1.2 | 1.2 | 1.198 | -0.001657 | -0.0001609 | -7.161e-05 | -2.681e-05 | -3.553e-05 | -2.021e-05 | -1.551e-05 | -1.581e-05 | -4.168e-06 | 0.0008425 | -1.916e-05 | -1.456e-05 | -1.365e-05 | -2.184e-06 | -1.555e-05 | -4.16e-06 | -6.118e-06 | -6.338e-06 | -6.612e-06 | 0.09436 | 1.198 | 1.2 | 1.2 | 1.2 | 1.2

## Slide 35: Conclusion
Machine learning provides viable approaches for improving simulation efficiency in EDA applications
Keep in mind: Learning is about learning
  The features, or
  The kernel function
The proposed learning approaches are generic and can be applied to diverse simulation contexts
We are developing the theories and concepts
  (1) for learning the kernel
  (2) for predicting the complex output objects

## Slide 36
Thank you
Questions?