## Slide 1: SVM-Based Routability-Driven Chip-Level Design for Voltage-Aware Pin-Constraint EWOD Chips
Qin Wang1, Weiran He, Hailong Yao1, Tsung-Yi Ho2, Yici Cai1
Tsinghua University
National Chiao Tung University

## Slide 2: Outline
Background
Problem Formulation
Contributions
Overall Design Flow
SVM-Based Electrode Clustering
Experimental Results
Summary

## Slide 3: Digital Microfluidic Biochips (DMFB)
DMFB is one of the many different types of biochips
Based on electrowetting-on-dielectric (EWOD) technology
  Control the movement of the droplet
Advantages of DMFB
  Reduces sample/reagent consumption
  Reduces total analysis time
  Dynamically reconfigurable for different types of sequential experiments
As the size of DMFB becomes larger, CAD methods are becoming necessary

## Slide 4: View of the EWOD Chips
2D array of electrodes for controlling the droplet movement
Top view of 2D electrode array
Courtesy of K. Chakrabarty and F. Su [1]
[1] K. Chakrabarty and F. Su, “Digital Microfluidic Biochips”, CRC Press, 2006.
Cross-section View
Top View

## Slide 5: Co-Design of EWOD Chips
Fluidic Layer
Control Layer

## Slide 6: Addressing Schemes
Direct Addressing & Broadcast addressing
Conduction wires
Electrodes
Via
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
16
Control pins
1
2
3
1
4
5
6
7
2
10
9
8
4
5
8
1
Electrodes that share the same control pin
Direct Addressing
Control pins: 16
(b) Broadcast addressing
Control pins: 10

## Slide 7: Broadcast Addressing Scheme
Droplet
Spacing
High voltage to generate an electrical field
0
0
1
0
X
X
X
time
X
0
0
1
0
X
X
X
X
0
0
1
0
X
X
X
X
0
0
1
0
X
X
X
X
0
0
1
Pin of electrode
Wire
External control pins
Actuation sequence
0
0
X
X
X
0
0
X
X
X
1
0
0
1
0
1
0
0
1
0
0
1
0
0
1
0
1
0
0
1
7 pins -> 4 pins
Broadcast addressing
Electrode

## Slide 8: Regular CAD Flow of DMFBs
[2] T.-Y. Ho, K. Chakrabarty, and P. Pop, “Digital Microfluidic Biochips: Recent Research and Emerging Challenges,” Proc. of CODES+ISSS, 2011.

## Slide 9: Routing Failed Problem
[3] ACER: An Agglomerative Clustering Based Electrode Addressing and Routing Algorithm for Pin-Constrained EWOD Chips,” IEEE Trans. on CAD 2014.
Actuation Sequence
Compatible Graph
Electrode Addressing
Cluster Routing & Escape Routing
Routing Failed

## Slide 10: Trapped Charge Problem

## Slide 11: Outline
Background
Problem Formulation
Contributions
Overall Design Flow
SVM-Based Electrode Clustering
Experimental Results
Summary

## Slide 12: Problem Formulation
Given
  A set of electrodes, the actuation sequences, the preferred voltage values, a threshold voltage value, the maximum number of allowed control pins, and the control layer design rules.
Constraint
  Control pin constraint
  Routing constraint
  Broadcast-addressing constraint
  Voltage constraint
Objective
  Find a feasible routing solution from all of the electrodes to the control pins with minimized total routing cost.

## Slide 13: Outline
Background
Problem Formulation
Contributions
Overall Design Flow
SVM-Based Electrode Clustering
Experimental Results
Summary

## Slide 14: Contributions
The first SVM-based electrode addressing methods
  Improve the routability
  Improve the reliability induced by the trapped charge problem
  Feature Extraction
    General Features
    Context Features
    Cluster Features
Effective ripup and rerouting methods are adopted
Machine Learning
Prediction Model
Physical Design

## Slide 15: Outline
Background
Contributions
Problem Formulation
Overall Design Flow
SVM-Based Electrode Clustering
Experimental Results
Summary

## Slide 16: Overall Design Flow of Our Approach
Input:
A set of electrodes
Actuation sequences
Constraints
Clustering Stage
Routing Stage
Ripup & Rerouting

## Slide 17: Outline
Background
Contributions
Problem Formulation
Overall Design Flow
SVM-Based Electrode Clustering
Experimental Results
Summary

## Slide 18: Support Vector Machine(SVM)
SVM is related to statistical learning theory
Solving classification problem
Key area in machine learning
Maximal margin

## Slide 19: Training Flow of SVM-Based Clustering

## Slide 20: Feature Extraction
The major concern of supervised learning
Having a great influence on experimental results
Features of electrode addressing
  General Features
  Context Features
  Cluster Features
Harra feature in graphics

## Slide 21: General Features
Describe a electrode addressing solution in a global view
  Number of clusters
  Total area of bounding boxes
  Number of clusters with a single electrode
  Total area of bounding box overlap
Normalization
  Area of the chip
  Number of electrodes

## Slide 22: Context Features
Routing resource information
Congestion information
Computing the bounding box for each cluster
Dividing the whole chip into four quadrants
Each quadrant
collects information separately
Bounding box area
Overlap information
Proportion of overlap area

## Slide 23: Cluster Features
Describe a clustering solution in detail
  Number of electrodes on the edge of the chip
  Area of bounding box overlap for a cluster
  Area of bounding box for a cluster
Feature for trapped charge problem
  Extract feature from the definition of trapped charge problem

## Slide 24: Electrode Addressing Solution Evaluation
Number of used control pins
Total wire length
Denote the trapped charge problem
Routing completion rate before ripup & rerouting
Area of chip size
Number of electrodes

## Slide 25: Testing Flow of SVM-Based Clustering
Training Flow

## Slide 26: Outline
Background
Contributions
Problem Formulation
Overall Design Flow
SVM-Based Electrode Clustering
Experimental Results
Summary

## Slide 27: Testcases
Benchmark | Width | Height | Area | #E | Voltage(v)
amino-acid-1 | 6 | 8 | 1008 | 20 | 50
amino-acid-2 | 6 | 8 | 1008 | 24 | 50
protein-1 | 13 | 13 | 3136 | 34 | 50
protein-2 | 13 | 13 | 3136 | 34 | 50
dilution | 15 | 15 | 4096 | 54 | 50
multiplex | 15 | 15 | 4096 | 59 | 50
random-1 | 10 | 10 | 1936 | 20 | 50
random-2 | 15 | 15 | 4096 | 30 | 50
random-3 | 20 | 20 | 7056 | 60 | 50
random-4 | 30 | 30 | 15376 | 90 | 50
random-5 | 50 | 50 | 41616 | 100 | 50
random-6 | 50 | 50 | 41616 | 100 | 50
random-7 | 60 | 60 | 59536 | 150 | 50
Width: the width of the chip
Height: the height of the chip
Area: the routing area considering the routing grids between adjacent electrodes
#E: the number of electrodes
Voltage: the threshold voltage for trapped charge issue

## Slide 28: Experimental Results
ACER
  S.S.-Y.Liu,C.-H.Chang,H.-M.Chen,andT.-Y.Ho,“ACER:An Agglomerative Clustering BasedElectrode Addressing and Routing Algorithm forPin-Constrained EWOD Chips,” IEEE Trans. on CAD, vol. 33, no. 9, pp. 1316-1327, 2014.
SVM1
  General Features
  Context Features
  Cluster Features
SVM2
  General Features
  Context Features

## Slide 29: Routing Completion Rate Without Ripup & Rerouting
Chart: ACER & SVM2
| amino-acid-1 | amino-acid-2 | protein-1 | protein-2 | dilution | multiplex | random-1 | random-2 | random-3 | random-4 | random-5 | random-6 | random-7
ACER | 92.31 | 87.5 | 29.63 | 21.62 | 47.06 | 83.33 | 66.67 | 42.11 | 34.69 | 35.29 | 29.49 | 26.32 | 19.17
SVM2 | 83.27 | 90.78 | 75.32 | 49.66 | 50.58 | 84.64 | 86.2 | 69.85 | 48.16 | 47.25 | 30.37 | 39.77 | 39.21
2
Chart: SVM1 & SVM2
| amino-acid-1 | amino-acid-2 | protein-1 | protein-2 | dilution | multiplex | random-1 | random-2 | random-3 | random-4 | random-5 | random-6 | random-7
SVM1 | 88.31 | 79.85 | 64.8 | 51.48 | 34.54 | 88.48 | 84.6 | 71.48 | 39.89 | 27.98 | 37.95 | 38.81 | 25.13
SVM2 | 83.27 | 90.78 | 75.32 | 49.66 | 50.58 | 84.64 | 86.2 | 69.85 | 48.16 | 47.25 | 30.37 | 39.77 | 39.21
2
Average
ACER
47.32%
SVM2
56.33%
SVM1
56.41%
SVM2
61.16%

## Slide 30: Final Routing Completion Rate After Ripup & Rerouting
Chart: ACER & SVM2
| amino-acid-1 | amino-acid-2 | protein-1 | protein-2 | dilution | multiplex | random-1 | random-2 | random-3 | random-4 | random-5 | random-6 | random-7
ACER | 100 | 100 | 70.97 | 100 | 100 | 98.04 | 100 | 85.71 | 100 | 98.73 | 100 | 90.8 | 93.53
SVM2 | 100 | 100 | 100 | 100 | 100 | 100 | 100 | 100 | 100 | 100 | 100 | 100 | 100
2
SVM1 and SVM2 are both 100%
For some cases, ACER is not 100%
Average
ACER
95.21%
SVM1
100%
SVM2
100%

## Slide 31: Number of Ripup & Rerouting Iterations
Chart: ACER & SVM2
| amino-acid-1 | amino-acid-2 | protein-1 | protein-2 | dilution | multiplex | random-1 | random-2 | random-3 | random-4 | random-5 | random-6 | random-7
ACER | 1 | 1 | 30 | 8 | 16 | 6 | 3 | 30 | 10 | 30 | 25 | 30 | 30
SVM2 | 2 | 1 | 6 | 9 | 9 | 6 | 2 | 4 | 9 | 16 | 13 | 13 | 28
2
Chart: SVM1 & SVM2
| amino-acid-1 | amino-acid-2 | protein-1 | protein-2 | dilution | multiplex | random-1 | random-2 | random-3 | random-4 | random-5 | random-6 | random-7
SVM1 | 1 | 1 | 7 | 9 | 9 | 6 | 1 | 5 | 12 | 9 | 13 | 22 | 26
SVM2 | 2 | 1 | 6 | 9 | 9 | 6 | 2 | 4 | 9 | 16 | 13 | 13 | 28
2
Average
ACER
25
SVM2
9
SVM2
9
SVM1
9

## Slide 32: Number of Used Control Pins
Chart: ACER & SVM2
| amino-acid-1 | amino-acid-2 | protein-1 | protein-2 | dilution | multiplex | random-1 | random-2 | random-3 | random-4 | random-5 | random-6 | random-7
ACER | 14 | 17 | 22 | 45 | 44 | 50 | 15 | 18 | 57 | 78 | 90 | 90 | 120
SVM2 | 13 | 17 | 37 | 45 | 42 | 49 | 11 | 21 | 46 | 77 | 70 | 74 | 117
2
Chart: SVM1 & SVM2
| amino-acid-1 | amino-acid-2 | protein-1 | protein-2 | dilution | multiplex | random-1 | random-2 | random-3 | random-4 | random-5 | random-6 | random-7
SVM1 | 12 | 17 | 33 | 42 | 41 | 48 | 11 | 25 | 47 | 54 | 73 | 80 | 118
SVM2 | 13 | 17 | 37 | 45 | 42 | 49 | 11 | 21 | 46 | 77 | 70 | 74 | 117
2
Average
ACER
51
SVM2
48
SVM2
47
SVM1
46

## Slide 33: Total Wire Length
Chart: ACER & SVM2
| amino-acid-1 | amino-acid-2 | protein-1 | protein-2 | dilution | multiplex | random-1 | random-2 | random-3 | random-4 | random-5 | random-6 | random-7
ACER | 290 | 364 | 698 | 1135 | 1395 | 1394 | 453 | 1052 | 1926 | 3977 | 9039 | 8251 | 12976
SVM2 | 276 | 324 | 727 | 1108 | 1341 | 1411 | 458 | 898 | 2040 | 4801 | 6576 | 8034 | 11418
2
Chart: SVM1 & SVM2
| amino-acid-1 | amino-acid-2 | protein-1 | protein-2 | dilution | multiplex | random-1 | random-2 | random-3 | random-4 | random-5 | random-6 | random-7
SVM1 | 289 | 324 | 973 | 1190 | 1496 | 1372 | 429 | 979 | 2459 | 3433 | 6154 | 7455 | 12331
SVM2 | 276 | 324 | 727 | 1108 | 1341 | 1411 | 458 | 898 | 2040 | 4801 | 6576 | 8034 | 11418
2
Average
ACER
3304
SVM2
3032
SVM2
3043
SVM1
2991

## Slide 34: Running Time
Chart: ACER & SVM2
| amino-acid-1 | amino-acid-2 | protein-1 | protein-2 | dilution | multiplex | random-1 | random-2 | random-3 | random-4 | random-5 | random-6 | random-7
ACER | 0.05 | 0.07 | 12.6 | 1.59 | 4.7 | 0.46 | 0.21 | 9.27 | 7.24 | 37.76 | 331.89 | 383.34 | 2242.5
SVM2 | 0.32 | 0.34 | 3.52 | 1.42 | 3.42 | 1.29 | 0.33 | 1.42 | 8.94 | 239.64 | 987.17 | 312.43 | 462.6
2
Chart: SVM1 & SVM2
| amino-acid-1 | amino-acid-2 | protein-1 | protein-2 | dilution | multiplex | random-1 | random-2 | random-3 | random-4 | random-5 | random-6 | random-7
SVM1 | 0.66 | 0.52 | 0.63 | 1.34 | 3.12 | 2.05 | 0.25 | 1.86 | 38.66 | 191.26 | 1201.54 | 429.61 | 630
SVM2 | 0.32 | 0.34 | 3.52 | 1.42 | 3.42 | 1.29 | 0.33 | 1.42 | 8.94 | 239.64 | 987.17 | 312.43 | 462.6
2
Average
ACER
232.21s
SVM2
154.91s
SVM2
155.44s
SVM1
225.53s

## Slide 35: Trapped Charge
Chart: ACER & SVM2
| amino-acid-1 | amino-acid-2 | protein-1 | protein-2 | dilution | multiplex | random-1 | random-2 | random-3 | random-4 | random-5 | random-6 | random-7
ACER | 19 | 18 | 19 | 19 | 19 | 19 | 17 | 19 | 19 | 18 | 19 | 19 | 19
SVM2 | 14 | 15 | 12 | 17 | 18 | 14 | 13 | 11 | 12 | 16 | 17 | 12 | 18
2
SVM1 and SVM2 are similar
Average
ACER
19v
SVM2
15v

## Slide 36: Outline
Background
Contributions
Problem Formulation
Overall Design Flow
SVM-Based Electrode Clustering
Experimental Results
Summary

## Slide 37: Summary
The first SVM-based chip-level design flow
The routability and reliability are both improved
Real-life biochemical applications validate the presented method effectiveness
Thank you!