## Slide 1: TPL-aware displacement-driven detailed placement refinement with coloring constraints
Tao Lin and Chris Chu
Iowa State University

## Slide 2: Outline
Background
Problem definition
Proof of NP-Completeness
MILP formulation
Heuristic Algorithm
Experimental results
Conclusions

## Slide 3: Background
Triple patterning lithography(TPL)
  One of the most promising lithography technologies to sub 14-nm design
  Layout is partitioned into three masks
  Layout 2-color solution 3-color solution

## Slide 4: Previous works
TPL layout decomposition
  General layout (2-D)
    E.g. Yu et al. (ICCAD 12’, 14’), Kuang et al. (DAC’13)
  Standard cell based layout (1-D)
    E.g. Tian et al. (ICCAD’12)
TPL-aware detailed placement
  Layout is allowed to modified
  Standard cell based
    E.g. Yu et al. (ICCAD’13), Kuang et al. (ICCAD’14), Tian et al. (ICCAD’14)

## Slide 5: Flow of TPL-aware detailed placement
Build coloring solutions for each type of standard cells
Build a look-up table to find the minimal extra space between two standard cells
Co-optimize detailed placement and TPL conflicts, and stitches
Cell shifting
Cell flipping
Cell swapping

## Slide 6: Coloring constraint
The standard cells of the same type use the same coloring solution (Tian et al. ICCAD’13)
  Standard cells of the same type eventually have similar physical and electrical characteristics.
  Minimize the impact of process variation
  (a) without coloring constraint
  (b) with coloring constraint
B
C
C
B
B
B
C
C
B
B

## Slide 7: Problem definition
Input:
  An initial detailed placement
  A standard cell library, each type of standard cell has a number of coloring solutions
Output:
  A refined detailed placement
  Coloring solution for standard cells
Constraints:
  Cell ordering is fixed, only cell shifting is allowed
  The cells of the same type should use the same coloring solution.
  Eliminate TPL conflicts
Objectives:
  Minimize total cell displacement and stitches

## Slide 8: NP-Complete
Single-row version
  The placement only has one row
  Reduction from 3-coloring problem
  3-coloring instance Single-row instance
t1
t2
t3
t4
t1
t2
t0
t1
t3
t0
t2
t3
t0
t3
t4
3-coloring problem has feasible solution, if and only if,
no extra space is introduced in single-row version problem

## Slide 9: MILP formulation
Cost function:
  weighted sum of stitches count and total cell displacement
Constraints:
  the cells of the same type should use the same coloring solution
  maintain cell ordering
  remove TPL conflicts

## Slide 10: MILP example
Simple example
  Only one row
  Only two standard cells A and B
  A is on the left of B

## Slide 11: MILP example
Notation | Standard cell A | Standard cell B
width | Wa | Wb
Original x-coordinate | Oa | Ob
New x-coordinate | na | nb
displacement | da | db
Coloring solution | a1, a2 | b1, b2
Stitch count of coloring solution | S1, S2 | T1, T2
A’s color/B’s color | b1 | b2
a1 | E11 | E12
a2 | E21 | E22
Lookup table

## Slide 12: MILP example
Min: ( S1*a1 + S2*a2 + S1*b1 + S2*b2 )*α + β*(da + db)
Subject:
a1 + a2 = 1, b1 + b2 = 1
|na – Oa | <= da , |nb – Ob| <= db
nb – na >= (Wa + Wb) / 2 + E11*a1*b1 + E12*a1*b2 + E21*a2*b1 + E22*a2*b2
x * y => replace x * y by r, and add the following three constraints
r – x – y >= -1
r <= x
r <= y

## Slide 13: Motivation: pattern count
Simple example
A
B
C
A
A
B
C
A
Pattern | Count
AA | 0
AB | 0
AC | 2
BA | 2
BB | 0
BC | 0
CA | 1
CB | 1
CC | 0
A pair of two adjacent cells is called a pattern

## Slide 14: Motivation: pattern extra space
Optimize the inserted extra space in pattern
  Eliminate TPL conflicts
  Avoid cell overflow of row
  (a) without overflow in the row
  (b) overflow in the row
B
C
C
B
B
B
C
C
B
B

## Slide 15: Motivation: impact on cell displacement
  The impact on total cell displacement
  (a) original layout of one row placement
  (b) new layout of one row placement
B
C
C
C
C
B
C
C
C
C

## Slide 16: Methodology
Std cell lib
Detailed placement
Recognize important patterns
Tree-based heuristic
LP-based refinement
Estimate cell distribution
Calculate the factor of patterns on total cell displacement
Generate solution graph
Generate maximum spanning tree
Dynamic programming
End

## Slide 17: Factor on cell displacement of pattern
Estimate cell distribution
  Probabilistic method to estimate extra space between adjacent cells
  Optimize total cell displacement
(a) Original detailed placement
(b) After estimation of cell distribution (cell is inflated)
C
B
A
A
C
B
C
B
A
A
C
B

## Slide 18: Factor on cell displacement of pattern
Calculate the weight of adjacent pair
  The more important adjacent pairs have higher weight
  Shifting direction is the feature
    A simple heuristic
    (a) Original detailed placement
    (b) After estimation of cell distribution
C
B
A
A
C
B
C
B
A
A
C
B
2
1
0
1
2

## Slide 19: The weight of pattern
Count * extra space * factor on cell displacement

## Slide 20: Methodology
Std cell lib
Detailed placement
Recognize important patterns
Tree-based heuristic
LP-based refinement
Estimate cell distribution
Calculate the factor of patterns on total cell displacement
Generate solution graph
Generate maximum spanning tree
Dynamic programming
End

## Slide 21: Solution Graph construction
Solution graph(undirected graph)
  A node is: a type of standard cell
  An edge is: a pattern
  Cost of a node: stitch cost, pattern weight
    E.g. (A, A)
  Cost of a edge: pattern weight
    E.g. (A, B)

## Slide 22: Solution Graph
Pattern | Count | factor | Extra space | weight
(A, A) | 1 | 0 | a | 0
(C, B) | 2 | 2 | b | 4*b
(B, A) | 1 | 1 | c | 1*c
(A, C) | 1 | 1 | d | 1*d
A
B
C
4 x b
1 x c
1 x d
C
B
A
A
C
B
2
1
0
1
2
Choose coloring solutions to minimize 4*b + c + d and stitch counts

## Slide 23: Tree based heuristic
Sparse Graph
If it is a tree, dynamic programming can achieve “optimal” solution
  Ignore some edges which are not important

## Slide 24: Maximum spanning tree
Pattern | Count | factor | Δ | weight
(A, A) | 1 | 0 | 2 | 0
(C, B) | 2 | 2 | 0 | 0
(B, A) | 1 | 1 | 3 | 1
(A, C) | 1 | 1 | 4 | 1
A
B
C
4 x 0
1 x 3
1 x 4

## Slide 25: Dynamic programming
Example
  Bottom up construction
5
3
4
1
2
a1: :10
a2: :20
a3: :30
b1: :10
b2: :20
b3: :30
c1: a1, b1: 40
c2: a2, b3: 50
e1: c1, d1: 80
e2: c2, d3: 100
d1: :20
d2: :20
d3: :40

## Slide 26: Methodology
Std cell lib
Detailed placement
Recognize important patterns
Tree-based heuristic
LP-based refinement
Estimate cell distribution
Calculate the factor of patterns on total cell displacement
Generate solution graph
Generate maximum spanning tree
Dynamic programming
End

## Slide 27: LP-based refinement
Refinement
  Enumerate different coloring solutions for one standard cell type
  Other types’ coloring solutions are fixed
  The coloring solution of each cell is determined
    Minimizing total cell displacement can be formulated as a linear programming

## Slide 28: Experimental results
case | MILP |  |  |  | Heuristic |  |  |  | 
 | Disp (E5) | # conflict | # stitch | Time (s) | Disp | # conflict | # stitch | WL increase | Time (s)
alu70 | 2.88 | 0 | 610 | 1245 | 2.94 | 0 | 610 | 0.6% | 12
byp70 | 1.04 | 0 | 1134 | 739 | 1.04 | 0 | 1134 | 0.0% | 21
div70 | 1.60 | 0 | 1136 | 3042 | 1.60 | 0 | 1136 | 0.1% | 28
ecc70 | 2.76 | 0 | 258 | 13 | 2.90 | 0 | 258 | 0.0% | 4
efc70 | 0.28 | 0 | 671 | 429 | 0.31 | 0 | 671 | 0.0% | 6
ctl70 | 0.45 | 0 | 275 | 351 | 0.48 | 0 | 275 | 0.0% | 10
top70 | 4.95 | 0 | 4731 | 3165 | 5.12 | 0 | 4731 | 0.0% | 326
Norm | 0.97 | 1.00 | 1.00 | 207 | 1.00 | 1.00 | 1.00 | 0.8% | 1

## Slide 29: Conclusions
Formulate a new TPL optimization problem considering TPL coloring constraints
Prove this new problem is NP-complete
Propose a MILP formulation
Propose an effective heuristic method

## Slide 30: Q & A