## Slide 1: From 2D to Monolithic 3D:
Design Possibilities, Expectations and Challenges
O. Billoint1, H. Sarhan1, I. Rayane2, M. Vinet1,
P. Batude1, C. Fenouillet-Beranger1, O. Rozeau1,
G. Cibrario1, F. Deprat1, O. Turkyilmaz1,
S. Thuries1, F. Clermidy1
1Univ. Grenoble Alpes, F-38000 Grenoble, France
CEA, LETI, MINATEC Campus, F-38054 Grenoble, France
2Mentor Graphics, 110 rue Blaise Pascal, 38330 Montbonnot-Saint-Martin, France

## Slide 2: Outline
Why 3D, Why Now?
What is Behind 3D-VLSI (Monolithic 3D)?
Design Possibilities
Expectations and Challenges
Conclusion

## Slide 3: Context
Chart: Number of Design Rules (Extracted from PDKs)
| 0,35um | 130nm | 65nm | 28nm | 14nm
Number of Design Rules | 500 | 1000 | 2000 | 5000 | 16000
Chart: Delay of a single wire of the same circuit (s) (extracted from internal DRMs)
| 28nm | 14nm | 10nm | 7nm
 | 1.2624e-13 | 2e-13 | 3.3948e-13 | 5.1975e-13
Scaling is about to be more and more complex
Back End performances are decreasing
TSV [1]
Size : 10x10um2
Pitch : 30um
HD-TSV [1]
Size : 0,85x0,85um2
Pitch : 1,75um
Cu-Cu [1]
Size : 1,7x1,7um2
Pitch : 2,4um
3D-VLSI (28nm) [2]
Size : 0,05x0,05um2
Pitch : 0,11um
Energy Efficiency
3D Interconnect Technology
[1] Patti B., Tezzaron, inc. « Implementing 2.5D and 3D Devices »
AIDA workshop 2013
[2] Taken from internal Design Rules Manual
3D Physical implementation
might be an alternative

## Slide 4: Going 3D for What?
Reduce Footprint
Reduce Wirelength
Reduce Power
Increase Yield?
Reduce Clock Period
Two half-size circuits better than a full size one?
True if :
Vertical connections have ~100% yield
Circuits are not fabricated sequentially
Are we able to test half of a design during process?!

## Slide 5: Interconnect Flavors
Reduce Footprint
Reduce Wirelength
Reduce Power
Increase Yield?
Reduce Clock Period
Two half-size circuits better than a full size one?
LDPC IP
28nm FDSOI
50% footprint reduction
Inter-Tier vias: 5439
Chart: Area Overhead (% of 3D Footprint) due to 3D Interconnect for a LDPC IP
| TSV | HD-TSV | Cu-Cu | Monolithic 3D
LDPC | 21449.0628 | 72.9864 | 37.274 | 0.28837
Minimize
3D interconnects
Technology | Size | Pitch
TSV (1) | 10µm | 30µm
HD-TSV (1) | 0,85µm | 1,75µm
Cu-Cu (1) | 1,70µm | 2,4µm
3D-VLSI 28nm (2) | 50nm | 110nm
[1] Patti B., Tezzaron, inc. « Implementing 2.5D and 3D Devices »
AIDA workshop 2013
[2] Taken from internal Design Rules Manual
Back to 2D footprint but with a 3D design!

## Slide 6: A 3D Solution for Everyone?
[2] 2014
TSV
[1] 2004
Cu-Cu
[1] Black, B. ; Nelson, D.W. ; Webb, C. ; Samra, N., « 3D processing technology and its impact on iA32 microprocessors »
Computer Design: VLSI in Computers and Processors, 2004. ICCD 2004.
[2] « Samsung Starts Mass Producing Industry’s First 3D TSV Technology Based DDR4 Modules for Enterprise Servers »
Seoul, Korea on Aug. 28. 2014
?
201x
3D-VLSI
Research
15% Power savings
15% Performances gain
50% Footprint reduction
Commercial

## Slide 7: Outline
Why 3D, Why Now?
What is Behind 3D-VLSI (Monolithic 3D)?
Design Possibilities
Expectations and Challenges
Conclusion

## Slide 8: CMOS Sequential Integration
Batude P. et al, « Demonstration of low temperature 3D sequential FDSOI integration down to 50nm gate length »
In Proceedings of IEEE Symposium on VLSI Technology, 2011
CoolCubeTM process developed at LETI
Regular «Hot» CMOS Process
Specific «Cold» CMOS Process
CoolCubeTM
Inter-Tier vias
28nm node
Size: 50x50nm2
Pitch: 110nm
Like a contact
Tungsten Back-End
Copper Back-End

## Slide 9: CoolCubeTM Flavors
Gate (Standard Cell) Level
Transistor Level
Compatible with 2D P&R
Not Compatible with 2D P&R
Process Boosters Friendly
(SiGe / III-V / …)
Different Node / Process Stacking
Requires Standard Cells redesign
No Standard Cells redesign
One MOS type on each tier
CMOS on each tier
Not Mainstream right now
Lot of intra-cell 3D vias
Lower standard cell density
Heterogeneous oriented

## Slide 10: CoolCubeTM Process Opportunities
Homogeneous / Heterogeneous Integration
Logic
--------------
Memory
Analog
--------------
Logic
Sensor
--------------
Logic
Soi
--------------
Cmos
Soi
--------------
Finfet
Soi
--------------
Soi
Sensor
--------------Analog
--------------Logic
--------------
Memory

## Slide 11: Outline
Why 3D, Why Now?
What is Behind 3D-VLSI (Monolithic 3D)?
Design Possibilities
Expectations and Challenges
Conclusion

## Slide 12: Design Possibilities
Homogeneous / Heterogeneous Integration
Logic
--------------
Memory
Analog
--------------
Logic
Sensor
--------------
Logic
Soi
--------------
Cmos
Soi
--------------
Finfet
Soi
--------------
Soi
Sensor
--------------Analog
--------------Logic
--------------
Memory
Predictive Design Kit
(Full Custom Analog dedicated)
2D Design Platform
(For Digital Design)
Basic Models, Parasitic Extraction, Layout
Plenty of 2D files for 2D tools!
1st order study : Ring Oscillators, small blocks
Detailed Studies (Performances, Power, Area…)

## Slide 13: 3D-VLSI Using Predictive DK
3D 14nm FDSOI Predictive DK
Turkyilmaz, O. et al « 3D FPGA using high-density interconnect Monolithic Integration »
in Design, Automation and Test in Europe Conference and Exhibition (DATE), 2014
Application to FPGAs
LB: Logic Block
SB: Switch Box
CB: Connection Box
CRAM : configuration RAM

## Slide 14: 3D-VLSI Using 2D Design Platform
Deflate / Inflate Standard Cells to emulate 3D placement
Single tier routing at a time
Extraction of timing informations tier by tier
Timing Analysis outside of P&R tool
Splitting / Folding Methodology to emulate 3D placement
Tier to Tier routing in one single run
Timing-Driven routing
Single Tool Methodology
[1]
[2]
Useful methodologies to get some trends and concepts but then…
[1Shreepad P. et al, « Design and CAD Methodologies for Low Power Gate-level Monolithic 3D ICs »
In proceedings of ISLPED’14, August 11–13, 2014, La Jolla, CA, USA
[2] Billoint O. et al, « A Comprehensive Study of Monolithic 3D Cell on Cell Design Using Commercial 2D Tool »
In Proceedings of DATE’15, Grenoble, France

## Slide 15: Outline
Why 3D, Why Now?
What is Behind 3D-VLSI (Monolithic 3D)?
Design Possibilities
Expectations and Challenges
Conclusion

## Slide 16: Expectations
[1] Dr. Karim Arabi, Qualcomm, Inc. “Keynote: Mobile Computing Opportunities, Challenges and Technology Drivers”, 51st Design Automation Conference (DAC), 2014.
1 process node advantage
PPA Gains
  30% Power savings
  40% Performances gain
  52% Footprint reduction
Market Expectations [1]

## Slide 17: Challenges
Which cell on which tier?
Design for Test (How do you test ½ chip?)
Process corners
Thermal behavior and workaround

## Slide 18: 3D Benefits Compared to Scaling
How do we optimize?
Cut the long wire(s)!
Distribute cells on tiers
…
Is there a possible better ring oscillator in 3D?
A
Z
A
B
Z
A
Z
A
Z
A
Z
Start
3D Interconnect cost has to be evaluated compared to Wire cost
Scaling benefits were
(digital) design independent
3D Stacking benefits may be architecture dependent

## Slide 19: Tier to Tier Interconnections (1)
Trade Wirelength for
vertical connection
What’s the cheapest solution for point to point connection, wire or via stack?
Chart: Horizontal versus Vertical Routing @ 28nm
| 0.185 | 0.36499999999999999 | 0.54499999999999993 | 0.72499999999999987 | 0.9049999999999998 | 1.1849999999999998 | 1.5799999999999998 | 2.3949999999999996 | 3.8749999999999996 | 6.2050000000000001
Vertical Routing (vias) | 3 | 6 | 9 | 12 | 15 | 18 | 21 | 21.4 | 21.8 | 21.82
Horizontal Routing (Wires) | 1.7575 | 3.4675 | 5.1775 | 6.8875 | 8.5975 | 11.2575 | 15.01 | 22.7525 | 36.8125 | 58.9475
Above 2,5µm length, is it REALLY worth trading wires for vias?

## Slide 20: Tier to Tier Interconnections (2)
Trade Wirelength for
vertical connection
What’s the cheapest solution for point to point connection, wire or via stack?
Chart: Horizontal versus Vertical Routing @ 28nm
| 0.185 | 0.36499999999999999 | 0.54499999999999993 | 0.72499999999999987 | 0.9049999999999998 | 1.1849999999999998 | 1.5799999999999998 | 2.3949999999999996 | 3.8749999999999996 | 6.2050000000000001
Vertical Routing (vias) | 3 | 6 | 9 | 12 | 15 | 18 | 21 | 21.4 | 21.8 | 21.82
Horizontal Routing (Wires) | 1.7575 | 3.4675 | 5.1775 | 6.8875 | 8.5975 | 11.2575 | 15.01 | 22.7525 | 36.8125 | 58.9475
Above 2,5µm length, is it REALLY worth trading wires for vias?
Tungsten resistivity = 6x Copper resistivity
Chart: Horizontal versus Vertical Routing @ 28nm
| 0.185 | 0.36499999999999999 | 0.54499999999999993 | 0.72499999999999987 | 0.9049999999999998 | 1.1849999999999998 | 1.5799999999999998 | 2.3949999999999996 | 3.8749999999999996 | 6.2050000000000001 | 7.2050000000000001 | 8.2050000000000001
Vertical Routing (vias) | 3 | 6 | 9 | 12 | 15 | 18 | 21 | 21.4 | 21.8 | 21.82 | 78.82 | 135.82
Horizontal Routing (Wires) | 1.7575 | 3.4675 | 5.1775 | 6.8875 | 8.5975 | 11.2575 | 15.01 | 22.7525 | 36.8125 | 58.9475 | 68.4475 | 77.9475
Tungsten Back-End for bottom tier solves contamination issues (process) but creates constraints on tier to tier optimization
Adding 1µm of Tungsten routing
Adding 2µm of Tungsten routing

## Slide 21: 3D-VLSI Concept and Area Ratio
Tungsten resistivity = 6x Copper resistivity
How many long wires to cut do we have?
[1] Karypis, G., Aggarwal, R., Kumar, V., and Shekhar, S. “Multilevel hypergraph partitioning: applications in VLSI domain”, Very Large Scale Integration (VLSI) Systems, IEEE Transactions on, 1999, 7(1), 69-79.
[2] Physical Aware Partitioning developed at LETI
hMetis [1]
PAP (40-60) [2]
2D
Reconfigurable FFT
Aiming at 50/50 Area Ratio may not always be the best solution for optimal PPA!
Trade Wirelength for
vertical connection

## Slide 22: Inter-Tier Power Distribution
Y-direction routing obstructions
Intra-Core power supply connections are mandatory to limit IR Drop
Wire Length and Power Consumption will be affected
Connecting to top tier Power Distribution is the cheapest solution

## Slide 23: Outline
Why 3D, Why Now?
What is Behind 3D-VLSI (Monolithic 3D)?
Design Possibilities
Expectations and Challenges
Conclusion

## Slide 24: Conclusion
Process is on the way!
ENABLING 3D-VLSI
50% Area reduction
Tier-Specific Process Corner Specification
3D Interconnects are critical
Inter-Tier Power Supply Distribution
Full 3D Routing in one run with Timing Closure
Tier-to-Tier Cell Placement Optimization
…etc
Power Optimization
I/Os and ESDs
Area Ratio
Thermal Behavior

## Slide 25: Conclusion
Scaling was design independent
3D stacking might be different
Wirelength reduction is a good goal to pursue as Back End performances have started decreasing
Preliminary studies using commercial 2D tools (trustable) for what they’re not supposed to do
Showing the real potential of 3D-VLSI will require to tape-out, measurements, comparisons…
And don’t forget that… 2 tiers is only the very beginning!

## Slide 26
O. Billoint1, H. Sarhan1, I. Rayane2, M. Vinet1, P. Batude1, C. Fenouillet-Beranger1, O. Rozeau1, G. Cibrario1, F. Deprat1, O. Turkyilmaz1, S. Thuries1, F. Clermidy1
1Univ. Grenoble Alpes, F-38000 Grenoble, France
CEA, LETI, MINATEC Campus, F-38054 Grenoble, France
2Mentor Graphics, 110 rue Blaise Pascal, 38330 Montbonnot-Saint-Martin, France

## Slide 27: Thank You