## Slide 1
Accelerated Path-Based Timing Analysis with MapReduce
Tsung-Wei Huang and Martin D. F. Wong
Department of Electrical and Computer Engineering (ECE)
University of Illinois at Urbana-Champaign (UIUC), IL, USA
2015 ACM International Symposium on Physical Design (ISPD)
Notes: ECE Main Slide

## Slide 2
Outline
Path-based timing analysis (PBA)
  Static timing analysis
  Performance bottleneck
  Problem formulation
Speed up the PBA
  Distributed computing
  MapReduce programming paradigm
Experimental result
Conclusion

## Slide 3
Static Timing Analysis (STA)
Static Timing analysis
  Verify the expected timing characteristics of integrated circuits
  Keep track of path slacks and identify the critical path with negative slack
Increasing significance of variance
  On-chip variation such as temperature change and voltage drop
  Perform dual-mode (min-max) conservative analysis
Notes: We all know STA is an important step in the design flow.

## Slide 4
Timing Test and Verification of Setup/Hold Check
Sequential timing test
  Setup time check
    “Latest” arrival time (at) v.s. “Earliest” required arrival time (rat)
  Hold time check
    “Earliest” arrival time (at) v.s. “Latest” required arrival time (rat)
Passing (positive slack)
Earliest rat
(hold test)
time
Latest rat
(setup test)
Hold violation 
No violation 
Setup violation 
Failing
Failing
Notes: One important task of the STA is the sequential timing tests which verifies the timing using setup/hold guard.

## Slide 5
Two Fundamental Solutions to STA
Block-based timing analysis
  Linear topological propagation
  Worst quantities for each point
  Very fast, but pessimistic
Path-based timing analysis
  Analyze timing path by path instead of single points
  Common path pessimism removal (CPPR), advanced on chip variation (AOCV), etc
  Reduce the pessimism margin
  Very slow (exponential number of paths), but more accurate
*Source: Cadence Tempus white paper
Notes: There are two fundamental solutions to the STA. The first one is the so called, block-based timing analysis, which performs linear topological scan on the circuit and propagate the timing based the topological order. During the propagation, we keep track of the “worst” timing quantities on each point…

## Slide 6
CPPR Example – Data Path Slack with CPPR Off
Pre common-path-pessimism-removal (CPPR) slack
  Data path 1: ((120+(20+10+10))-30) – (25+30+40+50) = -15 (critical)
  Data path 2: ((120+(20+10+10))-30) –(25+45+40+50) = -30 (critical)

## Slide 7
CPPR Example – Data Path Slack with CPPR On
Post common-path-pessimism-removal (CPPR) slack
  Data path 1: ((120+(20+10+10))-30) – (25+30+40+50)+5 = -10 (critical)
  Data path 2: ((120+(20+10+10))-30) –(25+45+40+50)+40 = 10
+5
+40
CPPR 1
CPPR 2

## Slide 8
Example: Impact of Common-Path-Pessimism Removal (CPPR)

## Slide 9
Problem Formulation of PBA
Consider the key coding block of PBA
  After block-based timing propagation
  Early/Late delay on edges
Input
  A given circuit G=(V, E)
  A given test set T
  A parameter k
Output
  Top-k critical paths in the design
Goal & Application
  CPPR from TAU 2014 Contest
  Speed up the PBA time
Benchmark from TAU 2014 CAD contest
Clock tree

## Slide 10
Key Observation of PBA
Time-consuming process but…
  Multiple timing tests (e.g., setup, hold, PO, etc) are independent
  Graph-based abstraction isolates the process of each timing test
  High parallelism
Multi-threading
  Shared-memory-based architecture
  Single computing node with multiple cores
Distributed computing
  Distributed-memory-based architecture
  Multiple computing nodes + multiple cores
  Goal of this paper!

## Slide 11
Conventional Distributed Programming Interface
Advantage
  High parallelism, multiple computing nodes with multiple cores 
  Performance typically scales up as the core count grows 
MPI programming library
  Explicitly specify the details of message passing 
  Annoying and error-prone 
  Very long development time and low productivity 
  Highly customized for performance tuning 
MPI_Init
MPI_Send
MPI_Recv
MPI_Isend
MPI_Irecv
MPI_Reduce
MPI_Scatter
MPI_Gather
MPI_Allgather
MPI_Allreduce
MPI_Barrier
MPI_Finalize
MPI_Grid
MPI_Comm
MPI …
Notes: The distributed programming is advantageous in … The conventional programming interface to distributed computing is the MPI library.

## Slide 12
MapReduce – A Programming Paradigm for Distributed System
First introduced by Google in 2004
  Simplified distributed computing for big-data processing
Open source library
  Hadoop (Java), Scalar (Java), MRMPI (C++), etc.
Notes: Because of this problem on MPI, Google first introduces the concept of MapReduce. MapReduce is a programming paradigm that simplifies distributed computing for big-data processing.

## Slide 13
Standard Form of a MapReduce Program
Map operation
  Partition the data set into pieces and assign work to processors
  Processors generate output data and assign each string a “key”
Collate operation
  Output data with the same key are collected to an unique processor
Reduce operation
  Derive the solution from each unique data set
MPI_Isend…
MPI_Irecv…
MPI_SEND…
M…
MPI_Send…
MPI_Recv…
MPI_Barrier…
…
Tradition MPI program
(> 1000 lines)
MapReduce program (<10 lines)

## Slide 14
Example - Word Counting
Count the frequency of each word across a document set
  3288 TB data set
  10 min to finish on Google cluster

## Slide 15
MapReduce Solution to PBA (I)
Map
  Partition the test set across available processors
  Each processor generates the top k critical paths
  Each path is associated with a global key (identical across all paths)
Collate
  Aggregate paths with the same key and combine them to a path string
Reduce
  Sort the paths from the path string and output the top k critical paths
Mapper (t)
Generate the search for test t
Find top k critical paths for t
Emit K-V pair for each path
Reducer (s)
Parse path from path string s
Sort paths
Output the top k critical paths

## Slide 16
MapReduce Solution to PBA (II)
Mapper
  Extract the search graph for each timing test
  Find k critical paths on each search graph [Huang and Wong, ICCAD’14]
Reducer
  Sort paths according to slacks and output the globally top-k critical paths
Input circuit graph
Map
Reduce
Top-1
critical path
Extraction of graph and paths

## Slide 17
Reducing the Communication Overhead
Messaging latency to remote node is expensive
Data locality
  Each computing node has a replicate of the circuit graph
  No graph copy between the master node and slave nodes
Hidden reduce
  Reducer call on each processor before the collate method
  Reduce the amount of path strings passing through computing nodes
*Source: Intel clustered OpenMP white paper

## Slide 18
Experimental Results
Programming environment
  C++ language with C++ based MapReduce library (MR-MPI)
  2.26GHZ 64-bit Linux machine
  UIUC Campus cluster (with up to 500 computing nodes and 5000 cores)
Benchmark
  TAU 2014 CAD contest on Path-based CPPR
  Million-scale circuit graphs

## Slide 19
Experimental Results – Runtime (I)
Parameter
  Path count K
  Core count C
Performance
  Only ~30 lines on MapReduce
  x2 – x9 speedup by 10 cores
  Promising scalability

## Slide 20
Experimental Results – Runtime (II)
Runtime portion on Map, Collate, and Reduce
  Map occupies the majority of the runtime
  ~ 10 % on process communication
Communication overhead
  Grows as the path count increases
  ~15 % improvement with hidden reduce

## Slide 21
Experimental Results – Comparison with Multi-threading on a Single Node

## Slide 22
Conclusion
MapReduce-based solution to PBA
  Coding ease, promising speedup, and high scalability
  Analyzes million-scale graph within a few minute
Future work
  Investigate more EDA applications on cluster computing
  GraphX, Spark, etc.