## Slide 1: Force-Directed Placement of VLSI Circuits
PDF Solutions
March 31, 2014
Hans Eisenmann

## Slide 2: Timeline VLSI Placement at the EDA Institute
Global placement objective | Quadratic (Space, Gordian et. al) |  |  |  |  |  |  | Linearized quadratic (GordianL) |  |  |  |  |  | bounding box based, per-pin, linearized quadratic (Kraftwerk2) |  |  | 
Global placement overlap free constraint | constant repulsive forces between modules |  | repulsive force function btw modules (Space) |  |  | Partitioning with COG (Gordian) |  | multi region iterative bipartioning (GordianL) |  |  | Spatial distribution based forces (Kraftwerk, Kraftwerk2) |  |  |  |  |  | 
Final placement | Simple |  |  | transportation problem (Space) |  |  |  |  | network flow (Domino) |  |  |  |  |  | Dynamic Programming (Abacus) |  | 
Year | 1975 | 1980 |  |  | 1985 |  | 1990 |  |  | 1995 |  | 2000 | 2005 |  |  | 2010 | 2015
This Talk

## Slide 3: Illustration
Based on force directed method
Additional forces for overlap removal

## Slide 4: Quadratic Placement
Formulation as a quadratic minimization problem
Solution of linear equation system
Analogy
  Nets as springs
  Solution: Equilibrium
C · p + d = 0

## Slide 5: Additional Forces
Additional force working on each cell
Placement determined by calculating the state of equilibrium
Access to complete solution space
  One-to-one map between forces and places
C · p + d + d´ = 0

## Slide 6: Spatial Representation
Map modules and placement area onto a spatial representation
  Supply demand model, no circular additional forces
Use convolution to achieve a global orientation
  Computational efficient
Two cells and their placement area
Spatial representation
After convolution Gradient gives the forces
Images: courtesy Bernd Obermeier

## Slide 7: Iterations
Placement
Spatial representation
Convo- luted
Gradient
Start with placement without additional forces
  Repeat:
  Update forces according to placement
  Calculate equilibrium as new placement
Until even distribution

## Slide 8: Properties
Geometrical flexibility
  Straightforward modeling of
    cell boxes
    non-rectangular cells (macro and mixed block placement)
    Non-rectangular placement area
Images: courtesy Peter Spinderl

## Slide 9: Properties
Geometrical flexibility
  Straightforward modeling of
    cell boxes
    non-rectangular cells (macro and mixed block placement)
    Non-rectangular placement area
No hard decision
  Decisions are revocable, not dependent on making an early decision
  Allows concurrent changes
Continuous
  Small changes of input data result in small changes of placement

## Slide 10: Timing
Longest path without timing optimization
Longest path with timing optimization

## Slide 11: Properties
Geometrical flexibility
  Straightforward modeling of
    cell boxes
    non-rectangular cells (macro and mixed block placement)
    Non-rectangular placement area
No hard decision
  Decisions are revocable, not dependent on making an early decision
  Allows concurrent changes
Continuous
  Small changes of input data result in small changes of placement
Updates of data is easy
  Various optimization goals can be applied to an quasi-legal placement
    ECO, timing, congestion, heat distribution and other metrics

## Slide 12: Timing Optimization For Legal Placement
Runtime (ns)
Iterations
Without timing optimization
With timing optimization right from the beginning
Timing optimization after creating a quasi-legal placement

## Slide 13: Heat Optimization
Non heat-aware placement
Heat aware placement
Images: courtesy Bernd Obermeier

## Slide 14: Placement Area Change Of Quasi-Legal Placement
Given situation: Macrocell at the left
Desired result: Macrocell at the right

## Slide 15: Layout Verification Algorithms Revisited
Hans Eisenmann, PDF Solutions
March 31, 2015
A Tribute to Kurt Antreich
an algorithm from the early EDA era

## Slide 16: Motivation Layout Verification
Todays layouts undergo a complex series of checking and modification steps
  DRC, retargeting, OPC, mask making
This happens at all stages of the process
  Often performed in iterations: Run, fix, run again
  Used from early design to tape-out and during manufacturing
Layout verification algorithms are the workhorse for this
Runtimes can be in the days, even in highly parallel compute environments.
Layout verification is not an optimization problem! The correct answer is known. All what counts is speed.
!

## Slide 17: Algorithmic Approaches
Global placement optimization | Quadratic (Space, Gordian et. al) |  |  |  |  |  |  |  | Linearized quadratic (GordianL) |  |  |  |  |  | bounding box based, per-pin, linearized quadratic (Kraftwerk2) |  |  | 
Global placement overlapfree constraint | constant repulsive forces between modules |  |  | repulsive force function between modules |  |  | Partitioning with COG (Gordian) |  | multi region iterative bipartioning (GordianL) |  |  | Spatial distribution based forces (Kraftwerk, Kraftwerk2) |  |  |  |  |  | 
Final placement | Simple |  |  |  | transportation problem (space) |  |  |  |  | network flow (Domino) |  |  |  |  |  | Dynamic Programming (Abacus) |  | 
Year | 1975 | 1980 |  |  |  | 1985 |  | 1990 |  |  | 1995 |  | 2000 | 2005 |  |  | 2010 | 2015
Layout verification | Bitmap based |  | Scanline based |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Before 1981, bitmap based approaches were the state of the art
After 1981, scanline based approaches were the state of the art
Layout synthesis Placement research from the institute in Munich
Worldwide academia and industry
This Talk
Start of Munich EDA Institute

## Slide 18: Bitmap Based
Represent layout as bitmap
Perform operation on bitmap
Boolean OR
001111111111100000000
000000000000000000000
001111111111100000000
001111111111111000000
001111111111111000000
001111111111111000000
000000001111111000000
000000001111111000000
000000000000000000000
Characteristics: Matrix style arrangement, matrix element represents area
001111111111100000000
000000000000000000000
001111111111100000000
001111111111111000000
001111111111111000000
001111111111111000000
000000001111111000000
000000001111111000000
000000000000000000000

## Slide 19: Variable Bitmap
Variable bitmap approaches use only existing coordinates
Boolean OR
0 0 0 0 0
0 1 1 0 0
0 1 1 1 0
0 0 1 1 0
0 0 0 0 0

## Slide 20: Edge Based Scanline
Sort Edges according to Y start coordinates
Move a “scanline” from bottom to top
Have edges on the scanline (active edges) sorted by X
Check and resolve when edges start, end or cross
Characteristics:
Edge representation
scanline divides into past, present, future
N log N complexity

## Slide 21: Comparison
Compared to scanline approaches, bitmap approaches are
Memory consuming
Constraint to rectilinear geometries
Slow
 | This fits today’s layout style
Memory consuming | Store partitioned rectangles and do bitmap conversion on the fly
Slow | Competitive speed for today’s layout styles

## Slide 22: Matrix Based Representation
Matrix element represent vertical edges
  In addition to the edge information, it has a net index and a polygon index for each edge
0
+1
0
+1
+1
+1
0
0
0
0
-1
0
0
-1
0
-1
-1
0
0
0
Use
matrix style from bitmap
edge representation from scanline

## Slide 23: Matrix Based Edge Representation
0
3
0
3
2
2
0
0
0
0
Alternatively, represent start edges only with width as attribute
Results in less column
3
2

## Slide 24: Matrix Based Operation
0
3
0
3
2
2
0
0
0
0
0
3
3
2
2
0
0
0
3
3
2
0
0
0
0
0
3
0
0
0
Scan from left to right
Rows are independent. In example below we process them bottom-up

## Slide 25: Matrix Based Operation
0
0
3
0
3
2
2
0
0
0
0
3
3
2
2
0
0
0
0
2
2
0
0
0
0
2
2
0
0
0
2
0
0
Rows can be calculated independently, thus:
Arrange data consecutive in columns to give fast data access
Process column by column, each column bottom up
Enables vectorization computations (in this example, two calculations at the same time)

## Slide 26: Experimental Results
Testcase: Mixture of product styles, technologies and compute intensive layers, each layout is run with 27 combinations of two-layer booleans.
Physical verification tool
from a major EDA vendor
Matrix based approach
Load and layout prep
Two layer booleans
Write-out
Runtime

## Slide 27: Experimental Results
Standard hardware (Xeon E5-2630), standard language/compiler (gcc-4.9.3). No hardware specifics such as inline assembler, instruction intrinsics or similar.
Benchmark | Tech | Layers | Speed-Up Total Runtime | Speed-Up Two layer OP
Testchip | 28 nm | Up to M2 | 2.0 | 2.5
Product chip (logic/SRAM) | 20 nm | Up to M1 | 2.5 | 3.1
Random stdcell placement | 14 nm | Up to M1 | 2.8 | 3.2