## Slide 1: ISPD 2015 Detailed Routing-Driven Placement Contest with Fence Regions and Routing Blockages
Ismail Bustany David Chinnery Joseph Shinnerl Vladimir Yutsis
www.ispd.cc/contests/15/ispd2015_contest.html

## Slide 2: Outline
Motivation
Benchmarks
Evaluation metrics
Results
Acknowledgements

## Slide 3: 1. Motivation

## Slide 4: Why another placement contest?
Increasing complexity of design rules
  Miscorrelation between global routing (GR) and detailed routing (DR)
  Global routing does not adequately consider short nets that are within global routing cells
Placement constraints impacting routability
  Floorplan: irregular placeable area, narrow channels between blocks
  Design rules: min-spacing, pin geometry, edge-type, and end-of-line
Example routability challenges for placement
  Netlist: high-fanout nets, data paths, timing objectives
  Routing: non-default rules, routing layer restrictions and blockages
Notes: Additional constraints beyond the ISPD 2014 benchmark suite are highlighted in green.

## Slide 5: Is global routing congestion a sufficient metric?
more evenly spread
GR edge overflow & node congestion
DR violations
Placement
with GR response
0.4% GR edge overflow
0.0% GR edge overflow
67 DR shorts
55 DR shorts
Notes: Example placements for the mgc_fft_2 design from the ISPD 2014 contest.

## Slide 6: Why impose a density limit?
Placement with 95% density limit, detail routed wire length 46.3m.
worse routing congestion
Cell spreading is needed for timing optimization, as cell sizing and buffering will increase area usage
Can also help reduce routing congestion
Example: mgc_superblue11 placements with different density limits and corresponding global routing congestion maps showing detailed routing shorts
Even spread placement with 65% density limit, detail routed wire length 53.6m.

## Slide 7: 2. Benchmarks

## Slide 8: Benchmarks
They are based on designs originally provided by
  Intel in the ISPD 2013 gate sizing contest
  IBM in the DAC 2012 routability-driven placement contest
They are adapted from the 2014 ISPD Detailed Routing-Driven Placement Contest’s benchmark suites A and B
There are 20 designs in this year’s contest
  16 were available to contestants
  4 blind benchmarks

## Slide 9: What was added in 2014?
Enhancements for the 2014 contest:
Added representative sub-45nm design rules, e.g.: edge-type, min spacing, end-of-line, non-default routing
Rectangular and rectilinear pin shapes, some metal2 pins
Added a power and ground mesh
  Pin access can be blocked by this if it is not considered
Restricted routing layers to increase routing difficulty
Use detailed routing as the final arbiter of quality

## Slide 10: What have we added this year?
Increased floorplan area to add large macros with routing blockages and narrow placement channels to the Intel benchmarks
  These help simulate top-level place-and-route problems
  The Intel benchmark suite previously had no macros
Fence placement regions (e.g. voltage regions)
  All cells assigned to a region must be placed within it, no other cells are allowed in.
  A region may be disconnected, consisting of several non-abutting rectilinear pieces.
Maximum density limit
  Some submitted 2014 ISPD placement contest solutions had local area utilization of 100% to minimize wirelength
  Reserve space for cell sizing and buffering in a place-route flow
  Penalty to detailed wire length score if density limit is violated

## Slide 11: Retained benchmark characteristics
 |  |  |  |  |  | %Area Utilization |  | 
Design | # Macros | # Cells | # Nets | # Fence Regions | # Primary Inputs & Outputs | Standard Cells | Standard Cells & Macros | Density Limit %
mgc_des_perf_1 | 0 | 112,644 | 112,878 | 0 | 374 | 90.6 | Same | 90.6
mgc_fft_1 | 0 | 32,281 | 33,307 | 0 | 3,010 | 83.5 | Same | 83.5
mgc_fft_2 | 0 | 32,281 | 33,307 | 0 | 3,010 | 49.9 | Same | 65.0
mgc_matrix_mult_1 | 0 | 155,325 | 158,527 | 0 | 4,802 | 80.2 | Same | 80.2
mgc_matrix_mult_2 | 0 | 155,325 | 158,527 | 0 | 4,802 | 79.0 | Same | 80.0
mgc_superblue12 | 89 | 1,286,948 | 1,293,413 | 0 | 5,908 | 44.0 | 57.0 | 65.0
mgc_superblue14 | 340 | 612,243 | 619,697 | 0 | 21,078 | 55% | 77% | 56.0
mgc_superblue19 | 286 | 506,097 | 511,606 | 0 | 15,422 | 52% | 81% | 53.0
Eight designs were retained from the 2014 ISPD contest, but we added a maximum density limit constraint – NEW!
Blind benchmarks are shown in red!
Notes: Note: the number of nets excludes the two power/ground nets, vdd and vss.

## Slide 12: Modified benchmarks this year
 |  |  |  |  |  | %Area Utilization |  | 
Design | # Macros | # Cells | # Nets | # Fence Regions | # Primary Inputs & Outputs | Standard Cells | Standard Cells & Macros | Density Limit %
mgc_des_perf_a | 4 | 108,288 | 110,281 | 4 | 374 | 56.7 | 71.7 | 56.7
mgc_des_perf_b | 0 | 112,644 | 112,878 | 12 | 374 | 56.3 | 49.7 | 56.3
mgc_edit_dist_a | 6 | 127,413 | 131,134 | 1 | 2574 | 54.1 | 61.6 | 54.1
mgc_fft_a | 6 | 30,625 | 32,088 | 0 | 3,010 | 28.5 | 74.0 | 50.0
mgc_fft_b | 6 | 30,625 | 32,088 | 0 | 3,010 | 30.9 | 74.0 | 60.0
mgc_matrix_mult_a | 5 | 149,650 | 154,284 | 0 | 4,802 | 44.9 | 76.8 | 60.0
mgc_matrix_mult_b | 7 | 146,435 | 151,612 | 3 | 4,802 | 34.2 | 72.6 | 60.0
mgc_matrix_mult_c | 7 | 146,435 | 151,612 | 3 | 4,802 | 32.7 | 72.6 | 60.0
mgc_pci_bridge32_a | 4 | 29,517 | 29,985 | 4 | 361 | 64.0 | 50.8 | 64.0
mgc_pci_bridge32_b | 6 | 28,914 | 29,417 | 3 | 361 | 27.3 | 50.6 | 27.3
mgc_superblue11_a | 1,458 | 925,616 | 935,613 | 4 | 27,371 | 35.1 | 73.0 | 65.0
mgc_superblue16_a | 419 | 680,450 | 697,303 | 2 | 17,498 | 50.2 | 73.9 | 55.0
Blind benchmarks are shown in red.
These twelve designs incorporate the new modifications (shown in green) applied to the 2014 ISPD benchmarks

## Slide 13: ISPD 2015 floorplans – Suite A
ISPD 2015 Floorplans
Variant A
Variant B
mgc_edit_dist
mgc_des_perf
mgc_fft
mgc_matrix_mult
mgc_pci_bridge32
Benchmark
placement blockage
macro
separate regions
disconnected region
LEGEND:
mgc_matrix_mult_c
ISPD 2014
Floorplans
Notes: mgc_matrix_mult_c is a blind benchmark.

## Slide 14: ISPD 2015 floorplans – Suite B
mgc_superblue11_a
mgc_superblue12
mgc_superblue16_a
placement blockage
macro
separate regions
disconnected region1
disconnected region2
disconnected region3
disconnected region4
LEGEND:
mgc_superblue14
mgc_superblue19
Notes: mgc_superblue14 and mgc_superblue19 are blind benchmarks.

## Slide 15: Disconnected fence regions
Disconnected regions are difficult as the placer has to decide which portion to place cells in
No team produced a routable placement for this design
Design | # Cells | # Nets | #Regions | Cells Area Utilization
mgc_edit_dist_a | 127,413 | 131,134 | 1 | 54.1%
a single disconnected region

## Slide 16
3. Evaluation metrics

## Slide 17: Total score S = min{SDP + SDR + SWL , 50}
These quantities add to the total score S for a placement:
DP : average legalization displacement in standard cell row heights of the 10% most displaced of all cells
WL’ : detail-routed wirelength, weighted by a density limit violation penalty – NEW!
  Scaled linearly from WL’min to 1.5xWL’median to [0,25]
DR : the number of detailed-routing violations,
  DR from 0 to 10,000 is scaled logarithmically (NEW!) to [0,25] by
  DR violations vary widely and log scaling better distinguishes intermediate scores

## Slide 18: Total score S = min{SDP + SDR + SWL , 50}
Placements receive the maximum score S = 50 if
There are fence region violations – NEW!
DP ≥ 25 standard cell rows
GR edge overflow exceeds GRedge_max of 0.3% for mgc_superblue designs and 3% for the other benchmarks
DR violations exceed 10,000

## Slide 19: Wire length scaling by density violations
The bins to analyze placement density are 8x8 standard cell row heights
The available area of bin b is
For regions, the density limit is
The overflow for bin b is calculated from the area of movable cells c in it:
Total density overflow fof as a dimensionless fraction of total cell area:
Scaled wirelength,
This is different from ISPD 2006 and our paper – corrected here!

## Slide 20: Example raw scores for pci_bridge32_a which has rectilinear regions
Legalization displacement 0.0
Detailed routing violations 260.8
Detail routed wire length 0.836m
Density overflow 0.42, so WL’ = WL x 1.42
GR edge overflow 0.12%
GR node overflow 112
Violation Type | Count | Weight | Contribution
cut proj. space | 7 | 0.2 | 1.4
cut size | 4 | 0.2 | 0.8
end of line | 12 | 0.2 | 2.4
min diff space | 9 | 0.2 | 1.8
min hole | 2 | 0.2 | 0.4
short | 254 | 1.0 | 254.0
Detailed routing violations total: |  |  | 260.8
Notes: We originally proposed taking the square root of detailed routing violations, normalized by the median wire length. However, this resulted in little difference between scores when the median DR score was high.
Run time and memory usage were not scored this year. They were not needed as a tie-breaker between similar scores.

## Slide 21: Contest scores were published daily – heavy competition between teams!
Team activity during the competition
Density Overflow Factor | Global Routing |  |  | Detailed Routing |  | Scaled Scores |  |  | Total Score | Team
 | %Edge Overflows | Node Overflows | Wire Length (m) | Wire Length (m) | Detailed Routing Violations | SDP | SWL | SDR |  | 
0.017 | 0.001 | 84 | 4.50 | 4.66 | 7.0 | 0.00 | 0.00 | 0.37 | 0.4 | ispd07
0.009 | 0.023 | 933 | 5.00 | 5.20 | 111.8 | 0.00 | 4.04 | 4.07 | 8.1 | ispd01
0.088 | 0.015 | 1,080 | 4.43 | 4.61 | 179.0 | 0.84 | 2.22 | 5.56 | 8.6 | ispd11
0.150 | 0.127 | 2,657 | 4.70 | 4.93 | 1713.8 | 0.00 | 7.47 | 15.70 | 23.2 | ispd04
0.069 | 0.238 | 4,625 | 6.16 | 6.36 | 8853.4 | 0.00 | 16.42 | 24.35 | 40.8 | ispd10
0.066 | 10.399 | 66,123 | 29.08 |  |  |  |  |  | 50.0 | ispd02
Notes: Example from final benchmark scores for mgc_matrix_mult_a.

## Slide 22
4. Results

## Slide 23: Participation statistics
12 teams initially participated from Canada, China, France, Germany, Hong Kong, Taiwan, USA
7 final placer binary submissions
Rank | Prize
1st | $2,000
2nd | $1,000
3rd | $500
ID | University | Team Lead and Members | Advisor
1 | University of Calgary and University of Waterloo | Nima Karimpour Darav, Aysa Fakheri Tabrizi, David Westwick | Lalah Behjat Andrew Kennings
2 | Dresden University of Technology | Andreas Krinke,Sergii Osmolovskyi, Johann Kenctel, Matthias Thiele, Steve Bigalke | Jens Lienig
4 | Chinese University of Hong Kong | Wing-Kai Chow, Peisahn Tu, Jian Kuang, Zhiqing Liu | Evangeline Young
5 | University of Illinois | Chun-Xun Lin, Zigang Xiao, Haitong Tian, Daifeng Guo | Martin Wong
7 | National Taiwan University | Chau-Chin Huang, Sheng-Wei Yang, Chin-Hao Chang, Hsin-Ying Lee, Szu-To Chen, Bo-Qiao Lin | Yao-Wen Chang
10 | National Chiao Tung University | Ching-Yu Chin | Hung-Ming Chen
11 | National Chung Cheng University | Xin-Yuan Su | Mark Po-Hung Lin

## Slide 24: Comparison of detailed routing violations for best placement results in 2015 vs. 2014
*mgc_superblue11_a and mgc_superblue16_a have fence region constraints in the 2015 contest, but still have comparable results.
Significant improvement in most results versus last year!
Chart: Number of DR Violations
| mgc_des_perf_1 | mgc_fft_1 | mgc_fft_2 | mgc_matrix_mult_1 | mgc_matrix_mult_2 | mgc_superblue11* | mgc_superblue12 | mgc_superblue14 | mgc_superblue16* | mgc_superblue19
2014 | 1242.6 | 770 | 55.2 | 229.8 | 219.8 | 174.6 | 193.4 | 0.4 | 32.8 | 522.6
2015 | 11.2 | 22.4 | 51.8 | 5.4 | 123.6 | 62.4 | 95.4 | 0.4 | 177.6 | 678.8

## Slide 25: Detailed routing violation scores for the top three teams – lower is better!
Chart: Detailed Routing Violation Score
| mgc_des_perf_1 | mgc_des_perf_a | mgc_des_perf_b | mgc_edit_dist_a | mgc_fft_1 | mgc_fft_2 | mgc_fft_a | mgc_fft_b | mgc_matrix_mult_1 | mgc_matrix_mult_2 | mgc_matrix_mult_a | mgc_matrix_mult_b | mgc_matrix_mult_c | mgc_pci_bridge32_a | mgc_pci_bridge32_b | mgc_superblue11_a | mgc_superblue12 | mgc_superblue14 | mgc_superblue16_a | mgc_superblue19
ispd01 | 21.4 | 0 | 0 | 25 | 4.89 | 2.46 | 15.95 | 20.81 | 6.33 | 15.64 | 4.07 | 21.45 | 15.87 | 17.11 | 0.34 | 2.63 | 6.39 | 0.02 | 25 | 11.12
ispd04 | 15.61 | 17.38 | 0 | 25 | 10 | 2.59 | 11.02 | 20.38 | 23.54 | 23.78 | 15.7 | 24.45 | 22.05 | 6.95 | 0 | 3.13 | 25 | 0.08 | 25 | 25
ispd07 | 0.58 | 17.8 | 0 | 25 | 1.1 | 2.26 | 12.41 | 21.73 | 0.28 | 4.36 | 0.37 | 20.3 | 25 | 16.63 | 0.17 | 3.6 | 3.63 | 0.04 | 5.53 | 25
Placement quality was evaluated by detailed routing in Mentor Graphics’ Olympus-SoCTM place-and-route tool.

## Slide 26: Total scores for each design for the top three teams – lower is better!
Chart: Total Score
| mgc_des_perf_1 | mgc_des_perf_a | mgc_des_perf_b | mgc_edit_dist_a | mgc_fft_1 | mgc_fft_2 | mgc_fft_a | mgc_fft_b | mgc_matrix_mult_1 | mgc_matrix_mult_2 | mgc_matrix_mult_a | mgc_matrix_mult_b | mgc_matrix_mult_c | mgc_pci_bridge32_a | mgc_pci_bridge32_b | mgc_superblue11_a | mgc_superblue12 | mgc_superblue14 | mgc_superblue16_a | mgc_superblue19
ispd01 | 24.13 | 50 | 0 | 50 | 6.03 | 2.46 | 17.61 | 21.95 | 6.98 | 17.64 | 8.1 | 29.54 | 15.87 | 17.11 | 4.83 | 4.46 | 11.91 | 3.43 | 50 | 14.81
ispd04 | 20.76 | 17.38 | 2.23 | 50 | 13.84 | 6.4 | 11.93 | 21.4 | 29.02 | 30.32 | 23.17 | 27.73 | 22.4 | 8.39 | 0 | 3.13 | 50 | 0.87 | 50 | 50
ispd07 | 3.49 | 20.26 | 8.5 | 50 | 5.54 | 10.91 | 13.39 | 22.14 | 1.17 | 5.53 | 0.37 | 20.3 | 50 | 18.09 | 0.24 | 6.55 | 3.63 | 3.86 | 5.53 | 50
Total Score = min { SDP + SDR + SWL , 50}

## Slide 27: Final rankings!
Very competitive results with significant improvements as the contest progressed. Congratulations to all teams.
Each of the top four teams had at least one benchmark with fewer detailed routing violations than all other teams!
 |  | Number of Designs with |  |  |  | 
Place | Team | Unroutable | Fewest Detailed Routing Violations | Shortest Detail Routed Wire Length Scaled by Density Overflow | Best Score for Design | Total Score
1st | Team 7 | 3 | 9 | 7 | 9 | 299
2nd | Team 1 | 3 | 6 | 5 | 3 | 357
3rd | Team 4 | 4 | 5 | 5 | 7 | 439
4th | Team 11 | 11 | 1 | 2 | 0 | 714
5th | Team 10 | 13 | 0 | 0 | 0 | 794
6th | Team 5 | 17 | 0 | 0 | 0 | 937
7th | Team 2 | 20 | 0 | 0 | 0 | 1,000

## Slide 28
5. Acknowledgements

## Slide 29: Acknowledgements
Many thanks to the following colleagues for valuable insights and help (in alphabetical order):
  Chuck Alpert
  Yao-Wen Chang
  Wing-Kai Chow
  Chris Chu
  Kevin Corbett
  Nima K. Darav
  Azadeh Davoodi
  Clive Ellis
  Igor Gambarin
  John Gilchrist
  John Jones
  Andrew B. Kahng
  Ivan Kissiov
Professor Evangeline Young and her student Wing-Kai Chow generously provided their RippleDP detailed placer to the contest.
Dr. Wen-Hao Liu generously provided his NCTUgr global router to the contest.
  Alexander Korshak
  Shankar Krishnamoorthy
  Wen-Hao Liu
  Igor L. Markov
  Mustafa Ozdal
  Cliff Sze
  Liang Tao
  Alex Vasquez
  Natarajan Viswanathan
  Alexander Volkov
  Yi Wang
  Benny Winefeld
  Evangeline F. Y. Young

## Slide 30
Backup slides

## Slide 31: Appendix A: Sample design rules

## Slide 32: Place and routing challenges
Dense metal1 pins, pin accessibility, power/ground grid
Complex DRC rules: cut space, minimum metal area, end-of-line rules, double patterning rules, edge-type, etc.
Challenging to pre-calculate routable combinations
Easy to route
Harder to route
2 tracks available
many tracks available
No detail routing checks in contests prior to ISPD 2014!

## Slide 33: Minimum spacing rule
There is a required minimum spacing between any two metal edges.
The minimum spacing requirement depends on:
  The widths of the two adjacent metal objects.
  The parallel length between the two adjacent metal objects.
parallel lengths between adjacent metal objects

## Slide 34: End of line rule
EOL spacing applied to objects 1 and 2:
  As object 3 overlaps the parallel length from the top of edge 1, EOL spacing between objects 1 and 2 will be required.
  Object 3 must remain outside the parallel halo.
2
3
1

## Slide 35: Non-default routing (NDR) rule
Non-default routing rules may specify:
  Increased wire spacing for a net
  Increased wire width for a net
  Increased via (cut) number at selected junctions
NDR may be assigned to a cell pin for wires or vias connecting to it
NDR may or may not accompany increased pin width or specific non-rectangular pins
NDRs are specified in the floorplan DEF file but may be assigned to a pin in the cell LEF file

## Slide 36: Blocked pin access violation
A blocked pin cannot be reached by a via or wire without violations.
Metal1 pins under metal2 stripe are not accessible by via1 vias
Metal2 pin overlaps metal2 stripe
Metal2 pins with NDR assigned are placed too close to each other

## Slide 37: Min spacing and end-of-line spacing violation examples
Example minimum spacing and EOL spacing violations between routing objects in congested areas. Many such violations are in the vicinity of pins assigned an NDR rule.

## Slide 38: Appendix B: More benchmark details

## Slide 39: Industry standard data format
Each benchmark has five input files:
  floorplan.def: with unplaced standard cells, net connectivity, fixed I/O pins and fixed macro locations, and routing geometry
  cells.lef (physical LEF): detailing physical characteristics of the standard cells including pin locations & dimensions, macros, & I/Os
  tech.lef (technology LEF): design rules, routing layers, and vias
  design.v: flat netlist of cells, I/Os, & net connectivity (per floorplan)
  placement.constraints: specifies density limit % (non-standard)
Outputs from contestant’s placement tool:
  Globally placed DEF file with all standard cells placed
  No changes allowed in cell sizes or connectivity
  The Library Exchange Format (LEF) and Design Exchange Format (DEF) are detailed here: http://www.si2.org/openeda.si2.org/projects/lefdef

## Slide 40: Modifications to ISPD 2013 gate-sizing benchmark designs
Adapted five designs from the ISPD 2013 suite with a 65nm cell library
Added sub-45nm design rules (see Appendix B): edge-type, min-spacing, end-of-line, non-default rules (NDRs) for routing
Pin-area utilizations per cell of about 20%
L-shaped output pins on 8% of cells in 2 designs, and 2% of cells on 1 design
Cells were downsized to minimum area
One cell output pin on M2 to check ability to avoid power/ground rails
Five routing layers are available: M1, M2, M3, M4, and M5
  M5 is not allowed for mgc_fft_2 – NEW!
M1 is only for vias to metal1 pins, & is otherwise not allowed for routing
Added macros with narrow channels as place-and-route blockages, and enlarged the floorplan footprints from ISPD 2014 contest – NEW!
Added fence regions: e.g. single-disconnected region in mgc_edit_dist_a, and three non-rectangular regions in mgc_matrix_mult_c – NEW!
Added blockages to show how to simplify placement, e.g. mgc_fft_b – NEW!

## Slide 41: Modifications to the DAC 2012 routability benchmark designs
Adapted three designs from the DAC 2012 suite (mgc_superblue11, mgc_superblue12, and mgc_superblue16)
Added 28nm design rules
Pin-area utilizations per cell of about 3%
All pins are rectangular (no L-shaped pins)
Cells were left at their original sizes
Seven routing layers are available: M1, M2, M3, M4, M5, M6, and M7
M8 is allowed on mgc_superblue16 to reduce routing difficulty – NEW!
Fence regions were added – NEW!
  Four disconnected fence regions in mgc_superblue11_a
  One disconnected fence region and one non-rectangular fence region in mgc_superblue16_a

## Slide 42: Standard cell libraries for our benchmarks
mgc_edit_dist, mgc_des_perf, mgc_fft, mgc_pci_bridge32, & mgc_matrix_mult:
65nm technology
Routing pitch 200nm
10 routing tracks per cell row
All standard cells are one row high
Typical 65nm standard cell
Routing pitch 200nm
Row height 2000nm
Pin height 1000nm
Pin width 100nm
Routing pitch 100nm
Row height 900nm
Pin height 84nm
Pin width 56nm
Typical 28nm standard cell
mgc_superblue11_a, 12, 14, 16_a, and 19:
28nm technology
routing pitch 100nm
9 routing tracks per cell row
All standard cells are one row high

## Slide 43: Power/ground (PG) mesh
Suite A metal layer | M1 | M2 | M3 | M4 | M5
PG routing track utilization | 11% | 6% | 27% | 24% | 30%
mgc_superblue11, 12, 14, 16, & 19 | M1 | M2 | M3 | M4 | M5 | M6 | M7
PG routing track utilization | 0% | 1% | 5% | 8% | 5% | 9% | 5%
Dense PG meshes have been inserted in all benchmarks adding to routing difficulty and increasing realism
Each routing layer has uniformly spaced PG rails parallel to its preferred routing direction
Rail thickness is constant on each layer but varies by layer
PG routing-track utilization varies across layers and designs

## Slide 44: Appendix C: Evaluation details

## Slide 45: Detailed routing violation score DR
The weighted sum of detailed routing violations DR is computed from the number of violations vi of routing violation type i and weight wi in the table below
Design Violation Type | Weighting wi
Routing open | 1.0
Routing blocked pin | 1.0
Routing short | 1.0
Design rule check (DRC) violation | 0.2

## Slide 46: Why use a log scale for DR violations?
Square root has less difference in SDR when normalizing by large DRmedian
E.g. comparing DR of 100 vs. 1000, SDR differs by 5.4 with square root, but they differ by 9.2 with the log scale
Added 100 inside logarithm so there is not too much difference in DR scores with a small number of routing violations
Chart: Raw Detailed Routing Violations + 1
| 1 | 2 | 3 | 6 | 11 | 21 | 51 | 101 | 201 | 501 | 1001 | 2001 | 5001 | 10001
Linear | 0 | 0.0025 | 0.005 | 0.0125 | 0.025 | 0.05 | 0.125 | 0.25 | 0.5 | 1.25 | 2.5 | 5 | 12.5 | 25
Square Root | 0 | 0.25 | 0.35355 | 0.55902 | 0.79057 | 1.118 | 1.7678 | 2.5 | 3.5355 | 5.5902 | 7.9057 | 11.1803 | 17.6777 | 25
Log scale(DR+100) | 0 | 0.053909 | 0.10729 | 0.26434 | 0.51637 | 0.98779 | 2.1967 | 3.7553 | 5.9521 | 9.7074 | 12.9914 | 16.4947 | 21.3019 | 25.0039
Notes: Added +1 to raw Detailed Routing Violations as showing on a log scale.

## Slide 47: Placement legalization
Olympus-SoCTM legalization fixes these issues in placement DEF files:
Edge-type violations & overlaps between cells or with blockages
Cells not aligned on the standard cell rows
Cells with incorrect orientation
Cell pins that short to the PG mesh
Blocked cell pins that are inaccessible due to the PG mesh
DRC placement violations between standard cells
Significant legalization displacements are penalized (SDP score).
If there are cells outside their fence region, or cells inside a fence region that are not assigned to it, then the placement is invalid! – NEW!

## Slide 48: Affine scaling for wire length
Simple affine scaling [WL’min , 1.5xWL’median ]  [0,25] is used for wire length: where

## Slide 49: Appendix D: Contest result details

## Slide 50: All the teams!
ID | University | Team Lead and Members | Advisor
1 | University of Calgary & University of Waterloo | Nima Karimpour Darav, Aysa Fakheri Tabrizi, David Westwick | Lalah Behjat Andrew Kennings
2 | Dresden University of Technology | Andreas Krinke,Sergii Osmolovskyi, Johann Kenctel, Matthias Thiele, Steve Bigalke | Jens Lienig
3 | National Tsing Hua University | Chung-Yi Kao, Yu-Ming Sung, Pin-Xin Liao, Chen-Hong Lin, Chen-Yeh Yang | Ting-Chi Wang
4 | Chinese University of Hong Kong | Wing-Kai Chow, Peisahn Tu, Jian Kuang, Zhiqing Liu, | Evangeline Young
5 | University of Illinois | Chun-Xun Lin, Zigang Xiao, Haitong Tian, Daifeng Guo | Martin Wong
6 | Chung Yuan Christian University | Te-Jui Wang | Shih Hus Huang
7 | National Taiwan University | Chau-Chin Huang, Sheng-Wei Yang, Chin-Hao Chang, Hsin-Ying Lee, Szu-To Chen, Bo-Qiao Lin | Yao-Wen Chang
8 | Paris’6 Computer Science Lab | Gabriel Gouvine | Jean-Pau Chaput
9 | National Central University | Li-Yuan Pang, Yu-Shiun Wang | Tai-Chen Chen
10 | National Chiao Tung University | Ching-Yu Chin | Hung-Ming Chen
11 | National Chung Cheng University | Xin-Yuan Su | Mark Po-Hung Lin
12 | Texas A & M University | Zhiyang Ong | NA

## Slide 51: Total scores for each design for the top three teams – lower is better!
Close race for 2nd and 3rd, but Team 1 scored significantly lower on 3 designs (mgc_matrix_mult_1, mgc_superblue12, and mgc_superblue19)
Team 4 only scored significantly lower on 1 design (mgc_des_perf_a), and had one more unroutable placement for a design
Chart: Total Score
| mgc_des_perf_1 | mgc_des_perf_a | mgc_des_perf_b | mgc_edit_dist_a | mgc_fft_1 | mgc_fft_2 | mgc_fft_a | mgc_fft_b | mgc_matrix_mult_1 | mgc_matrix_mult_2 | mgc_matrix_mult_a | mgc_matrix_mult_b | mgc_matrix_mult_c | mgc_pci_bridge32_a | mgc_pci_bridge32_b | mgc_superblue11_a | mgc_superblue12 | mgc_superblue14 | mgc_superblue16_a | mgc_superblue19
ispd01 | 24.13 | 50 | 0 | 50 | 6.03 | 2.46 | 17.61 | 21.95 | 6.98 | 17.64 | 8.1 | 29.54 | 15.87 | 17.11 | 4.83 | 4.46 | 11.91 | 3.43 | 50 | 14.81
ispd04 | 20.76 | 17.38 | 2.23 | 50 | 13.84 | 6.4 | 11.93 | 21.4 | 29.02 | 30.32 | 23.17 | 27.73 | 22.4 | 8.39 | 0 | 3.13 | 50 | 0.87 | 50 | 50

## Slide 52: Team activity during the contest
Team activity
Activity by design
52