## Slide 1: FreePDK15 An Open-Source Predictive Process Design Kit for 15nm FinFET Technology
Kirti Bhanushali, W. Rhett Davis (NCSU)
International Symposium on Physical Design
April 1, 2015
NC STATE UNIVERSITY

## Slide 2: Motivation
Problem
  Restrictions on PDKs prevent sharing of design data, impede research & teaching
Solution
  Free Predictive PDK, establishes a baseline for research & teaching in design, architecture, manufacturing, and automation
FreePDK45 accomplished this for 45nm, FreePDK15 seeks to do the same for 15nm

## Slide 3: Process Cross Section
What everyone should know: FinFETs & MOL layers
Thanks to Alex Toniolo (NanGate) for suggesting layers
Schuddinck, et al (IEDM 2012) suggested dimensions
Si
Fins
Gate
AIL1
Active Interconnect Level-1 (AIL1)
AIL1
AIL2
AIL2
Active Interconnect Level-2 (AIL2)
GIL
Gate Interconnect Layer (GIL)
Layer Interconnect Overlap Level
Metal-1
Level-2 Contact to Metal-1
(Applies to AIL-2 and GIL)
FEOL
BEOL

## Slide 4: Width Quantization Of Active
Active width grows in increments of 40nm
  Weff = 2*Hfin + Wfin
  FinFETs have integer number of fins
48nm
88nm
128nm
40nm

## Slide 5: Planar Device vs. FinFET
Traditional planar
MOS
FinFET in Layout View
FinFET on Physical Mask
FINS
Fin Interconnect

## Slide 6: MOL Layers in Layout View
MOL Layers reduce resistance, improve density
Metal1
Interconnect to Power rails
Interconnect PMOS & NMOS
Vias for connecting higher metal layers to Gate and Active interconnects

## Slide 7: Multiple-Patterning Rules
Metal1A
Metal1B
Metal1A
Metal1A
36nm
36nm
54nm
Two colors for Gate, MOL, and 1X Metal Layers
Metal pitch for different colors is small
Metal pitch for the same color is larger
Optional uncolored layer post layout coloring (GATE only)
Also: Gate Cut Layer

## Slide 8: Other Restrictive Rules
Width and spacing is orientation-dependent, to account for off-axis illumination
AIL1, AIL2, GIL and GATE should not bend, to reduce pinching
Metal1A
Metal1A
28nm
56nm

## Slide 9: Layout – Inverter
Dummy Gate
AIL1
AIL2
GIL
Inverter Layout
Notes: 1:1 PMOS to NMOS

## Slide 10: NAND4
MINT1
M1B
GATEA
GATEB
NAND4 Layout

## Slide 11: Complex Layouts
Inverter cell
NAND4 cell
Complex Layouts

## Slide 12: Layout Density Comparison
FinFET inverter @14nm : MOS Inverter @45nm
  Ideal shrink factor- 1:9
  Achieved shrink factor- 1:6
FinFET layout density is 1.3x MOSFET (Alioto, ICM 2009)
Cause
  Width Quantization
  Higher Hfin for same Weff
Density Evaluation

## Slide 13: Comparison to NanGate Library
NanGate evaluation: Rules not dense enough
DRC errors for SDFFRNQ_X1 cell given below
Working with NanGate to revise rules

## Slide 14: Future Releases
LVS, PEX rules in development
Planned for release summer 2015
Semi Global M1x2
(130 nm thick)
Intermediate M1x1
(60 nm thick)
M1 (60 nm thick)
Global M1x4 (260 nm thick)
Metal 1 Pitch

## Slide 15: Licensing
Licensed for Academic Use under 3-clause BSD License
  Caveat: Cannot distribute a Cell Library until Summer 2016
Please contact us for commercial license
  Click through license may be possible with your help

## Slide 16: Conclusion
First-pass FreePDK15 with DRC is now available, including new 15nm features
  FinFETs
  MOL Layers
  Multiple Patterning
LVS & PEX rules available in summer
How you can help
  Feedback on design rules
  Request a commercial use license

## Slide 17: Acknowledgement
Alex Toniolo
Joseph Davis, Tarek Ramadan, Ahmed Hammed Fathy, Omar El-Sewefy , Ahmed El-Kordy, Hend Wagieh (Mentor Graphics)
Acknowledgements