## Slide 1
Open Cell Library in 15nm FreePDK Technology
Mayler Martins, Jody Matos, Renato Ribas, Andre Reis, Guilherme Schlinker, Lucio Rech and Jens Michelsen

## Slide 2: Outline
Part I - Layout
  Library Creation Flow
  Cell Template
  DFF Layout example
  Dummies and Diffusion Gaps
  Double patterning
  Design rule negotiation
Part II – Library Content
  Cells
  Available descriptions
Part III – Synthesis Example
Conclusion

## Slide 3: Standard Cell Creation Flow
Circuit Re-ordering
Transistor Placement/Routing
Library N
Circuit Synthesis
Topology Creation
Compaction
Characterization
View Export
Layout Creation
Library Definition

Block Benchmark
Specification

Circuit Synthesis
Cell N
Multiple Iterations

Layout Creation
Compaction
Verification
View Export
Library Definition
Topology Creation

Logic restructuring
Circuit optimization
Structural Layout generation
Simplified design rules
2D Cleanup Compaction
Migration to related technology
LVS, DRC, PEX
Parasitic extraction
.lib/LEF, GDSII, CDL
Verilog, Vital, Edif
OpenAccess
Block Level Evaluation of:
Design Rules Impact
timing
power
area
Cell Architecture
Cell Mix
Drive Strength/Skew Granularity
Rule adjustments
Block Benchmark
Q = !((A1 * A2) + B1)
Notes: Let the animation run after the first click, to shorten the number of clicks for this slide. Advise audience to watch for the full slide deck on this during Library Creator presentation

## Slide 4: Cell Template
Cell template is 12 track tall
Gate layer is regularly spaced
Dummy gates are inserted in the cell boundaries

## Slide 5: FFD Layout Example
This is an example of a DFF layout

## Slide 6: Dummy Gates

## Slide 7: Dummy Gates - 2
Dummy gates are necessary at cell boundaries

## Slide 8: Dummy Gates - 3
Only two successive gates can have contacts, dummy gates are used as spacers

## Slide 9: Diffusion Gaps
Diffusion Gaps (with at least one functional gate) can also be necessary

## Slide 10: Double Patterning

## Slide 11: Double Patterning

## Slide 12: Double Patterning

## Slide 13: Double Patterning

## Slide 14: Double Patterning

## Slide 15: Double Patterning

## Slide 16: Double Patterning

## Slide 17: Double Patterning

## Slide 18: Design Rule Negotiation
New design rules were introduced in the design kit during library development
This negotiation happens also during the development of real design kits
For example, design rules related to local interconnection layers were adapted to allow the use of these layers for routing intents
DFF Layout
Local Interconnection Layers

## Slide 19: Design Rule Negotiation
Another example is the introduction of Gate Cut layer, to allow two different transistors in the same poly layer
Tri-state Buffer layout
Gate Cut Layer

## Slide 20: Outline
Part I - Layout
  Cell Template
  FFD Layout example
  Dummies and Diffusion Gaps
  Double patterning
  Design rule negotiation
Part II – Library Content
  Cells
  Available descriptions
Part III – Synthesis Example
Conclusion

## Slide 21: Library Content - Cells
COMBINATIONAL CELLS |  |  |  | 
Cell Name | #In | Description | Drive Strengths | #Cells
BUF | 1 | Buffer cells | X1 to X16 | 6
INV | 1 | Inverter cells | X1 to X16 | 6
AND | 2, 3 and 4 | AND cells | X1 and X2 | 6
OR | 2, 3 and 4 | OR cells | X1 and X2 | 6
NAND | 2, 3 and 4 | NAND cells | X1 and X2 | 6
NOR | 2, 3 and 4 | NOR cells | X1 and X2 | 6
MUX2 | 3 | Multiplexer cell | X1 | 1
XOR | 2 | XOR cell | X1 | 1
XNOR | 2 | XNOR cell | X1 | 1
AOI | 3 and 4 | AND-OR-Inverter cells | X1 and X2 | 4
OAI | 3 and 4 | OR-AND-Inverter cells | X1 and X2 | 4
FA | 3 | Full-adder cell | X1 | 1
HA | 2 | Half-adder cell | X1 | 1
 |  |  | TOTAL | 49

## Slide 22: Library Content - Cells
SEQUENTIAL CELLS |  |  |  | 
Cell Name | #In | Description | Drive Strengths | #Cells
DFFRNQ | 3 | D flip-flop with asynchronous !reset | X1 | 1
DFFSNQ | 3 | D flip-flop with asynchronous !set | X1 | 1
SDFFRNQ | 5 | D flip-flop with scan and asynchronous !reset | X1 | 1
SDFFSNQ | 5 | D flip-flop with scan and asynchronous !set | X1 | 1
LHQ | 2 | High enable Latch | X1 | 1
 |  |  | TOTAL | 5

## Slide 23: Library Content - Cells
ADDITIONAL CELLS |  |  |  | 
Cell Name | #In | Description | Drive Strengths | #Cells
CLKBUF | 2 | Clock buffer cells | X1 to X16 | 6
TBUF | 2 | Tri-state buffer cells | X1 to X16 | 6
FILL | - | Filler cells | X1 to X16 | 5
CLKGATETST | 3 | Clock gate with test pin | X1 | 1
ANTENNA | - | Antenna cell | - | 1
FILLTIE | - | Cell to tie the wells | - | 1
TIEH | - | Tie-high cell | - | 1
TIEL | - | Tie-low cell | - | 1
 |  |  | TOTAL | 22

## Slide 24: Library Content - Cells
SUMMARY |  | 
Combinational cells |  | 49
Sequential cells |  | 5
Additional cells |  | 22
 | TOTAL | 76

## Slide 25: Library Content - Descriptions
View | File Extension | View Description
Technology Library | .lib | Provide logic, timing, power and area information of the cells in the library
Geometric Library | .lef | Provide information about the physical layout of the library in plain text, including design rules and abstract information about the cells
Simulation Library | .v | Provide a behavioral information of the cells for simulation intents
Cell Layouts | .gds | Provide information about planar geometric shapes, text labels, and other layout information in a binary format
Cell Netlists | .spi | Provide an instance-based transistor netlist, representing instances, nets, and some attributes
OpenAccess | .oa | Provide a database containing layouts and netlists

## Slide 26: Outline
Part I - Layout
  Cell Template
  FFD Layout example
  Dummies and Diffusion Gaps
  Double patterning
  Design rule negotiation
Part II – Library Content
  Cells
  Available descriptions
Part III – Synthesis Example
Conclusion

## Slide 27: Synthesis Example
 | 15nm | 45nm | Reduction
Library Characteristics |  |  | 
Operation Voltage (V) | 0.8 | 1.1 | N/A
Operation Frequency (GHz) | 1.0 | 1.0 | N/A
Characterization Corner | Typical | Typical | N/A
Area Results |  |  | 
Total Area (um²) | 21706.92 | 211068.87 | 89.7%
Cell Area (um²) | 15437.17 | 68566.29 | 77.5%
#Cells | 31442 | 36583 | 14.1%
Timing Results |  |  | 
Timing Slack (ps) | 307.5 | 0 | N/A
Power Results |  |  | 
Leakage Power (mW) | 0.542 | 1.365 | 60.3%
Dynamic Power (mW) | 37.767 | 94.919 | 60.2%
Total Power (mW) | 39.309 | 96.284 | 60.2%

## Slide 28: Conclusions
Complete and functional library provided in freePDK15 technology
Compatible with commercial tool formats
  Liberty, lef, verilog, gds, spice and openaccess files available
This library is a key enabler for research in physical design in advanced technology nodes
We believe this effort is very relevant for this community
Available for download at
  http://www.nangate.com/?page_id=22

## Slide 29
Thank you!
Questions?